## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN:21-04-0257-00-0000-draft_invariants
Title: Invariants in Proposed Drafts
Date Submitted: March, 16, 2004
Presented at IEEE 802.21 session #7 in Atlanta, GA
Authors or Source(s):
David Johnston
Abstract: This document attempts to identify draft text elements that are invariant under the current proposals and so clarify text that meets the needs outlined in all the proposals.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3: Services Proposed
Proposed services have evolved to a common position
  Information Service
    Request/Response
    Information orthogonal to, or typed by media
    Available locally or remotely
  Event Service
    Source initiated
    Consumed by MIH or upper interface of MIH
    Pass across locally up the stack or down and across the local link to pass up the remote stack
    Sourced within MIH, MIH Upper Interface, MAC or PHY

## Slide 4: Information Definition
Defined Services need information of the appropriate type
  Information service
    Information definition per media type
    Media independent information
    802.21 specific information
  Event Service
    Event types
    Event semantics
    Event scope (local/remote/both, bounds)

## Slide 5: Supporting Elements
Information and Event Service requires supporting elements
  LLC differentiated message definitions
    Ethertype
    Internal payload structure, message classes, bit level coding
    Addressing rules
  SAP Definitions
    Upwards to Layer 3
    Internal SAPs
      Only necessary for internal structuring. Not required
    Primitives for both

## Slide 6: Models
The proposed services demand a model to allow conceptualization of the usage. E.G.
  Feeding information to a policy engine
    Ethertype
    Internal payload structure, message classes, bit level coding
    Addressing rules
  Feeding information to upper layers
    Upwards to Layer 3
    Internal SAPs
      Only necessary for internal structuring. Not required

## Slide 7: Implications
Any given model is more restrictive than the service definitions and supporting material, since it imposes a mode of use that the specification should not enforce
E.G.
  Policy engine in MIH
  Policy engine above MIH
  Policy engine distributed horizontally or vertically
  These are different models and use but do not affect (mostly) the service, SAP or information definitions

## Slide 8: Draft Text
I expect the draft will be structures something like this:
  Introduction – Informative material, model assumptions
  Overview – Stack layering, interface locations
  Support Features
    Information base representation
    Event structure
    Ethertype
    Payload format
  Event service
    Event service upper interface primitive definitions
    Event service internal interface primtive definitions
  Information service
    Request/Response protocol
    Request/Response message defintions
    Upper interface primitive definitions

## Slide 9: The Models in Context
The policy engine is a consumer of events and information that may use that information to select the port to use, or select the point of attachment of an individual port
This is divisible into
  The bit that determines preference
  The bit that imposes, requests or otherwise effects a handover
It is the separation of these entities that leads to the only significant interface difference between the models

## Slide 10: The Models in Context
A simple binary decomposition of internal/external PE and internal/external control
  Model A, Internal PE and control
  Model B, External PE and control
  Model C, External PE, Internal control
  Model D, Internal PE, External control
Port selection
Port Preference
identification
MIH
events
Info req/rsp
events
Info req/rsp
802.11 (e.g)
802.16 (e.g.)
Single interface advertised upwards
L3
No preference or control signaling on SAP

## Slide 11: The Models in Context
A simple binary decomposition of internal/external PE and internal/external control
  Model A, Internal PE and control
  Model B, External PE and control
  Model C, External PE, Internal control
  Model D, Internal PE, External control
Port selection
Port Preference
identification
MIH
events
Info req/rsp
MIH
selection
L3
Control Signaling
On SAP!

## Slide 12: The Models in Context
A simple binary decomposition of internal/external PE and internal/external control
  Model A, Internal PE and control
  Model B, External PE and control
  Model C, External PE, Internal control
  Model D, Internal PE, External control
Port selection
Port Preference
identification
MIH
events
Info req/rsp
L3
Preference Signaling
On SAP!

## Slide 13: The Models in Context
MIH
A simple binary decomposition of internal/external PE and internal/external control
  Model A, Internal PE and control
  Model B, External PE and control
  Model C, External PE, Internal control
  Model D, Internal PE, External control
Port selection
Port Preference
identification
MIH
events
Info req/rsp
L3
Control Signaling
On SAP!

## Slide 14: Therefore
Differences in the proposals and associated models might be significant
But the difference in the text comes down to the presence of two forms of upper layer SAP primitives
  Control Imperatives, EG:
    Dot21_Select_Port_X
    Dot21_Change_attachment_Point
  Preference_Indicationss, EG:
    Dot21_Port_x_Preferred
    Dot21_Port_Weight_Map
It doesn’t effect the definition of the event service, information service, transport, information base or events
The presence of control imperative or preference indication does not impose their use.
Define them and all models are supported. No other text changes between the proposals -> 95% of text is common.