## Slide 1: Liaison Report IEEE 802.11 work related to 802.21
David Hunter
Vetronix / ETAS / Robert Bosch
hunter@timefactor.com

## Slide 2: 802.11 Groups related to 802.21
Ethernet Residential (proposed new 802 group)
  Previously requested 802.11, 802.15 to help with 802.3 interface, handover
802.11r – Fast BSS Transition
  Between BSSes within the same ESS
802.11u – Wireless Interworking with External Networks
  MAC changes to accommodate, among others, 802.21
  Stephen McCann, Chair, is coordinating with 802.21: reviewed 11-05-0279-00 earlier today
802.11v – Wireless Network Management
  Management protocol for STAs
  First meeting as a TG in January 2005; just beginning work now
Other candidates:
  802.11k – Performance Measurement (runtime metrics useful for decision making)
  802.11p – Automotive (note MAC address anonymity and rapid handover issues)

## Slide 3: Residential Ethernet
Impetus:
Trade association initiated
Moving toward standards development
  Creating parameterized QoS over Ethernet
  Study Group status; working on PAR and 5 Criteria
  Requesting coordination, help from 802 wireless groups
    Want to enable handoff of 802.3+QoS with 802.11, 802.15
    Michael Teener was going to coordinate 802.21 interface with Ajay
Questions
  Status of 802.3-related handover in the two current 802.21 proposals?
  Is support of this handover a requirement?

## Slide 4: 802.11r Update
Critical importance for 802.21
  Whatever 11r creates will definitely be required for 802.21's success
Voted on 8 proposals at the end of January meeting
Only two proposals reached 50% approval
  TAP and JIT
  All the others are excluded as standalone alternatives
    Though content can come back if merged with one of winning proposals
TAP: Transition Acceleration Protocol
JIT: Just In Time Association

## Slide 5: 802.11r Current Work
Postponed vote on proposed merged text until May 2005
Merging specific areas: identified about a dozen work areas
But three of these are critical to the others:
  Pre-roam negotiations – Over The Air vs. Over The DS
  Resource pre-allocation
  Key Hierarchy and Key Generation
Created ad-hoc groups to work on merging these
Most of work this week in these three ad-hoc groups
  First two mergers now complete: 11-05-0239-00
  Key hierarchy is a major continuing work topic: 11-05-0250-00

## Slide 6: 802.11r Current Status
11-05-0239-00 covers both delivery mech and pre-allocation
OTA vs OTD
  Answer is yes: technology needs to support both
  AP advertises whether it supports OTD
Supporting a concept of a "Mobility Domain"
  Subset of the Security Domain
  Set of all other 802.11 APs to which a STA can roam right now
Support pre-allocation of reservations
  Both direct to the next AP and through a proxy/broker
  Have laid out message types and formats

## Slide 7: 802.11r Timeline
March 2005 Piecemeal merging of TAP and JIT
April 20-22, 2005 Interim ad-hoc in Toronto
May 2005 Merged draft and vote to adopt
Bi-weekly teleconferences May 25 – July
  Considering additional detail proposals after Draft available
Still expect to go to letter ballot before 802.21 draft complete