## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-05-0248-00-0000
Title: MEDIA INDEPENDENT HANDOVER Functions and Services Specification
Date Submitted: March 14th, 2005
Presented at IEEE 802.21 session #NN in City
Authors or Source(s): Alan Carlton, Ulises Olvera-Hernandez, Marian Rudolf, Juan Carlos Zuniga, Michael Hoghooghi, Jeff Keating , Peretz Feder, Andrea Francini, Fang Hao, Ray Miller, Ajay Rajkumar, Sampath Rangarajan, Sameer Sharma, Yousif Targali, Rajio Salminen, Uri Goldstein
Abstract: Harmonized points
Summary of the key aspects of the Media Independent Handover Proposal

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3
Harmonized Points: Freescale, Interdigital, Lucent, Seesta
The group agrees that IEEE802.21 standard will support the existence of two transport modes. Ethernet based and network based. Ethernet transport for IEEE devices one hobp away (e.g. BS to IS) and network transport in support of cellular equipment and IS components residing in remote network elements.
The group agrees that the attached reference model applies to cellular and IEEE network elements
The group agrees that the Triggers 1) between the MIH and the LL, 2) between MIH and HL, and 3) between remote MIH entities should be NORMATIVELY defined in the 802.21 specification. This will include a full semantic definition of these triggers and their contents.
SAPs
  The group agrees that there should be new SAP(s) defined for the MIH layer itself.
  The group agrees to explore the usability of existing PHY and MAC SAPs as well as PMLE and MLME SAPs as part of the MIH interface. Investigation will attempt to expand existing ones as opposed to recreating new SAPs.
The group agrees that a broadcast capability is required for quick advertisement of MIH capability. This mechanism may take the form of a broadcast field or a few bits. The broadcast form will be media dependent and at a minimum just inform the terminal, by using a few bits, about its MIH capability. Once advertised, the mobile unit can query the IS for more pertaining information. Configuration of this capability can be done through a management entity or a remote network trigger. Changes in the media dependent elements (e.g. beacon enhancements) will be required to support this capability

## Slide 4: Harmonized Points: Freescale, Interdigital, Lucent, Seesta
The group agrees that the event reporting mechanisms of some media dependent elements (i.e. 802.11/16) will need to be enhanced in order to support the requirements of 802.21. While information such as RSSI and Power Level are captured in the media independent layers there is no STANDARD mechanism for defining how this information is reported (e.g. thresholds) to a higher layer (i.e. the MIH). Trigger support will be required that provides this configuration capability.
Informative section:
  Recommendations on Media/interface specific changes to MAC/PHY
  Example call flows to accomplish inter-technology handover
The group agrees that new SAPs are introduced when they pertain to the MIH layer. As such, MIH-SAP is introduced as a point of interface to the upper layers. All the triggers that are generated by the MIH, all the registration and deregistration primitives between the upper layers and MIH also belong to MIH-SAP. All inputs from lower layers into the MIH layer including the triggers are provided through the existing media specific SAPs such as MAC, PHY and LLC. Triggers generated by MIH typically controlling the PHY and MAC handovers, are part of the media specific MAC/PHY SAPs and already defined elsewhere. The MLME and PLME are part of media specific SAPs (i.e., part of 802.11 SAPs) and are defined elsewhere. In this MIH model upper layers need to register for events from lower Layers. This applies to upper layers registering for events from MIH and to MIH itself registering for events from media specific PHY and MAC. The reverse is not required. That is, lower layers do not register to events from upper layers as the MIH MUST be able to request a link switch to the lower layers. Switching requests given by the MIH to lower layers should not be ignored and therefore registration is not required.

## Slide 5: Harmonized Points: Freescale, Interdigital, Lucent, Seesta
The group agrees that the event reporting mechanisms of some media dependent elements (i.e. 802.11/16) may need to be enhanced in order to support the requirements of 802.21. While information such as RSSI and Power Level are captured in the media dependent layers there is no STANDARD mechanism for defining how this information is reported (e.g. at particular thresholds) to a higher layer entity. Triggers will be required to support the configuration of these reporting mechanisms.
The group agrees that a general trigger approach is preferable to a very specific trigger approach (i.e. one trigger per event). The group will define a general set of triggers that provides the full body of functionality required (e.g. Link_down, Link_available etc.) through primitives that carry these general trigger definitions. This approach should lead to a well optimized and efficient protocol design.
  For media-specific triggers that already exist, the primitive-to-trigger mapping (that is, primitive types used to carry these triggers) would be left unchanged.

## Slide 6
Reference Model (1 of 2)

## Slide 7
Reference Model (2 of 2)

## Slide 8
Evaluation Matrix