| Project | IEEE 802.21 Media Independent Handover Services <http://www.ieee802.org/21/> |
| --- | --- |
| Title | Link ID parameters to be added for all MIH primitives : LB Issue #47 |
| Date Submitted | September, 2006 |
| Source(s) | Eunah Kim, Junghoon Jee, Hongseok Jeon |
| Re: | IEEE 802.21 Session #NN in Melbourne |
| Abstract | This contribution proposes to add link ID parameters to all related MIH primitives |
| Purpose | Discuss and adopt in the draft. |
| Notice | This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21. |
| Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. |

1. Introduction

Issue #47, Comment #568

Comment

The MIH primitives do not include a link identifier. Thus there is no way for MIH users to specify the link of interest.

Suggested Remedy

add a link ID parameter to all MIH primitives

Resolution of Group

Rejected.

Some MIH primitives may refer to multiple link layer technologies. So there needs to be careful examination of all primitives where this needs to be added. Identified as an issue and listed in list, to be worked upon. Rejected since there is no definite/clear remedy.

2. Proposal

Link ID(s)

- Are no needed for MIH_Register, MIH_DeRegister Primitives

- Is needed to be added in MIH_Capability_Discover, MIH_Event_Register and MIH_Event_Deregister primitives.

- Already exist in all MIH event primitives.

- Is no needed for MIH_Get_Status primitives because they are used to discover the status of the currently connected and potentially available links, not the status of a certain link.

- Already exist in MIH_Switch.request primitives as OldLinkIdentifier and NewLinkIdentifier

- Already exists in MIH_Configure.request primitive, but is needed to be added in MIH_Configure.confirm primitive.

- Already exists in MIH_Scan.request primitive. According to Editor’s note, MIH_Scan.confirm will be modified to support confirming multi-link scan request.

- Already exist in MIH_Handover_Initiate and MIH_Handover_Complete primitives as CurrentLinkIdentifier.

- Is needed to be added in MIH_Handover_Commit and to be deleted in MIH_Handover_Prepare primitives (Refer to 21-06-0667-07-0000-Handover_Command_Update.doc)

- Already exist in MIH_Network_Address_Information primitives as CurrentLinkIdentifier.

- Is no needed for MIH_Get_Information primitives

New Suggested Remedy

- Change sections 7.4.2.1.2, 7.4.2.2.2, 7.4.3.1.2, 7.4.3.2.2, 7.4.4.1.2, 7.4.4.2.2, 7.4.8.1.2 as described below.

    - MIH Capability Discover

      - MIH_Capability_Discover.request

        - Semantics of service primitive

MIH_Capability_Discover.request			 	(

SourceIdentifier,

DestinationIdentifier,

LinkIdentifier,

SupportedEventList,

SupportedCommandList,

SupportedISQueryTypeList

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| ~snip~ Refer the D01.09 |  |  |  |
| Destination Identifier | Identifier | Valid MIHF identifier | The destination identifier of request or response. This is the identifier of local or peer MIHF. |
| LinkIdentifer | Link ID | N/A | Identifier of the link whose MIH capability is to be discovered |
| SupportedEventList | List | Set of supported events | List of supported events on the client |
| ~snip~ Refer the D01.09 |  |  |  |

      - MIH_Capability_Discover.confirm

        - Semantics of service primitive

MIH_Capability_Discover.confirm	 (

SourceIdentifier,

DestinationIdentifier,

LinkIdentifier,

SupportedEventList,

SupportedCommandList,

SupportedISQueryTypeList

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| ~snip~ Refer the D01.09 |  |  |  |
| LinkIdentifer | Link ID | N/A | Identifier of the link whose MIH capability is discovered. |
| SupportedEventList | List | Set of supported events | List of supported events on MIHF |
| ~snip~ Refer the D01.09 |  |  |  |

    - MIH Event Register

      - MIH_Event_Register.request

        - Semantics of service primitive

MIH_Event_Register.request	 (
				SourceIdentifier,

DestinationIdentifier,

LinkIdentifier,
				RequestedEventList
				)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| ~snip~ Refer the D01.09 |  |  |  |
| LinkIdentifer | Link ID | N/A | Identifier of the link for event registraton |
| RequestedEvent List | Set of Event IDs | Set of valid link events | List of link layer events that the end point would like to receive indications for, from the Event Source |

      - MIH_Event_Register.confirm

        - Semantics of service primitive

MIH_Event_Register.confirm	 (

LinkIdentifier,

ResponseEventList
				)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| LinkIdentifer | Link ID | N/A | Identifier of the link for event registraton |
| ResponseEvent List | Set of Event IDs and their registration status | Set of valid link events | List of link layer events along with their registration status |

    - MIH Event Deregister

      - MIH_Event_Deregister.request

        - Semantics of service primitive

MIH_Event_Deregister.request	 (
				SourceIdentifier,
				DestinationIdentifier,

LinkIdentifier,

RequestedEventList
				)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| ~snip~ Refer the D01.09 |  |  |  |
| LinkIdentifer | Link ID | N/A | Identifier of the link for event deregistraton |
| RequestedEvent List | Set of Event IDs | Set of valid link events | List of link layer events for which indica tions need to be deregistered from the Event Source |

      - MIH_Event_Deregister.confirm

        - Semantics of service primitive

MIH_Event_Deregister.confirm	(

LinkIdentifier,

ResponseEventList
				)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| LinkIdentifer | Link ID | N/A | Identifier of the link for event deregistraton |
| ResponseEvent List | Set of Event IDs and their Deregistration status | Set of valid link events | List of link layer events along with their deregistration status |

    - MIH Configure

      - MIH_Configure.confirm

        - Semantics of the service primitive

MIH_Configure.confirm (

SourceIdentifier,

DestinationIdentifier,

LinkIdentifier,

ConfigurationResponseSets

)

| Name | Type | Valid Range | Description |
| --- | --- | --- | --- |
| Source Identifier | Identifier | Any valid individual or group identifier | The identifier of entity where the request is initiated. This field may be optionally left empty if the command is local. |
| Destination Identifier | Identifier | Valid MIHF identifier | The destination identifier of request or response. This is the identifier of local or peer MIHF. |
| LinkIdentifer | Link ID | N/A | Identifier of the link configured |
| Configuration ResponseSets | Set of configu ration parame ters and their configuration results | N/A | Containing a set of configuration parameters and their corresponding configuration results: ConfigurationParameter ResultCode |