| Project | IEEE 802.21 MIHO <http://www.ieee802.org/21/> |
| --- | --- |
| Title | Indicating network types in a TLV query |
| Date Submitted | November 13, 2006 |
| Source(s) | Qiaobing Xie |  |
| Re: | IEEE 802.21 Session #17 in November 2006 |
| Abstract | This document proposes text for allowing TLV IS query to indicate network types |
| Purpose | LB#1a comment resolution comment #2192 |
| Notice | This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21. |
| Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. |

Discussion:

If an MN that does not have cdma2000-HRPD interface makes an IS query, it probably will want to tell the MIIS server not to include any cdma2000-HRPD information in the response. Therefore, there need to be a way for the querier to indicate what network technology(ies) should be included in a response.

Proposed changes to D02.00:

- Information Request

Information Request (from client to information server) shall carry an MIIS_TLV_QUERY TLV which contains: 1) an optional Querier Location TLV parameter indicating the location of the querier, and 2) an optional Reporting Template TLV, as shown below:

| Type=MIIS_TLV_QUERY | Length= Variable |
| --- | --- |
| Querier Location TLV [variable] (optional) |
| Coverage Types TLV [8 octet] (optional) |
| Reporting Template TLV [variable] (optional) |

The TLVs that are carried in the Information Request are described below.

Querier Location TLV is defined as follows:

| Type=MIIS_TLV_QUERIER_LOCATION | Length= Variable |
| --- | --- |
| The value is defined the same as that of PoA Location IE (see 6.3.5.3.2) |

Querier Location, if provided in the query, can be useful for the Information Server to refine its response. If not provided (for example, a UE does not have its location measurement when making the query), the Information Server shall either get the querier location information from other means or use best estimate of the querier’s location to generate the neighboring network information.

Coverage Types TLV is defined as follows:

| Type=MIIS_TLV_COVERAGE_TYPES | Length= 4 |
| --- | --- |
| The value is a 4 octet bitmap, as defined below: Bit #0: IEEE 802.3 (Ethernet) Bit #1: Wireless - Other Bit #2: Wireless - IEEE 802.11 Bit #3: Wireless - CDMA2000 Bit #4: Wireless - UMTS Bit #5: Wireless - cdma2000-HRPD Bit #6-31: Reserved (shall not be used and shall be always set to “0”) Note, the above definition shall be updated if the Network Type Representation in Table 8 is changed. |

Coverage Types TLV, if provided in the query, is used to indicate the coverage types the querier wants to include in the response. The querier indicates the coverage types it wants to include in the response by setting the corresponding bits to “1”. If not provided, the Information Server shall include all available coverage types in the response.

...

- Rules for Generating Returned IEs

Upon receipt of the query, the information server will:

1) create the list of neighboring access network information for the given location; If a Coverage Types TLV is provided in the query, include only the information of the neighboring access networks of the coverage types indicated in the Coverage Types TLV. Otherwise, include information of all available neighboring access networks for the given location.

2) if no Reporting Template TLV is given in the query, send the list of neighboring access network information in a List of Neighboring Access Networks Container in an Information Response.

3) if a Reporting Template TLV is given in the query, extract the requested IE(s)/Containers from the list of neighboring access network information using the rules from Section 6.3.6.1 and send them in an Information Response.