| Project | IEEE 802.21 MIHS <http://www.ieee802.org/21/> |
| --- | --- |
| Title | TLV Type Value Assignment |
| DCN | 21-07-0158-02-0000TLVTypeValues |
| Date Submitted | May 2007 |
| Source(s) | Miriam Tauil, Yoshihiro Ohba, Y. Alice Cheng, Subir Das, Kenichi Tanuchi |
| Re: | IEEE 802.21 Session #20 in Montreal |
| Abstract | IEEE P802.21/D05.00 defines the TLV type values per message. This method is not consistent with other IEEE 802 protocols and may increase implementation complexity. This contribution proposes defining the TLV type values once for the entire protocol. |
| Purpose | Adoption |
| Notice | This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein. |
| Release | The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that IEEE 802.2 may make this contribution public. |
| Patent Policy | The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development <http://standards.ieee.org/board/pat/guide.html>. |

# 1. Introduction

IEEE P802.21/D05.00 defines the TLV type values per MIH message. This method is not consistent with other IEEE 802 protocols, such as 802.11, 802.16, and 802.1 and may increase implementation complexity.

The complexity of defining the TLV types as in IEEE P802.21/D05.00 is a result of requiring 4 pieces of information (Service ID, Action ID, OpCode, TLV type) in order to specify the “actual TLV Type”.  This complexity may result in unnecessary extra efforts for implementation, debugging, interoperability testing and extendibility of the protocol.

This contribution suggests defining each TLV type value once for the entire protocol.

Using IEEE P802.21/D05.00 method, defining a new TLV applicable for a few messages requires new definition for each of these messages. On the contrary, the proposed method requires one definition for the new TLV type value.

In order to address previous comments related to definition clarity of similar TLVs, and avoid duplicated information in the specification (comment 4396), this document defines TLV type formats, which are being used for several TLVs.

The contribution is composed from the following sections. Section 2.1 specifies the TLV formats. Section 2.2 proposes line by line changes to sections 8.5 and 8.6 including TLV type definitions and MIH Messages and their related TLVs.

Annexes A and B contain the list of MIH messages that use MAC_ADDRESS TLVs and LINK_ID TLVs.

Section 2.2 does not contain changes related the Information Service (due to lack of time).

# 2. Proposed changes

This section shall be added in section 8.5, after the TLV type table.

# 2.1. Add definition of TLV formats:

# 2.1.1. MAC_ADDRESS format

The following specifies the MAC_ADDRESS format. It is being used for definition of several TLVs .

| Type | Length | Value |
| --- | --- | --- |
| Defined in the specific TLVs, that use this format. | Variable | A MAC Address. Encoded as Address base type of Diameter protocol (RFC3588). A link layer AddressType is encoded in the first 2-octet. |

# 2.1.2. LINK_ID format:

The following specifies the LINK_ID format. It is being used for definition of several TLVs.

| Type | Length | Value |
| --- | --- | --- |
| Defined in the specific TLVs, that use this format. | Variable | Consisting of the following TLVs - Link Type - Mobile Node MAC Address - PoA MAC Address (optional) |

The embedded TLVs are defined as the follows:

- Link type:

| Type | Length | Value |
| --- | --- | --- |
| 12 | 4 | One of the valid Type value defined in Table 9. |

- Mobile Node MAC Address:

| Type | Length | Format |
| --- | --- | --- |
| 11 | Variable | MAC_ADDRESS |

- PoA MAC Address:

| Type | Length | Format |
| --- | --- | --- |
| 10 | Variable | MAC_ADDRESS |

2.1.3.MIHF_ID format:

The following specifies the MIHF_ID format. It is being used for definition of Source MIHF_ID and Destination MIHF_ID.

| Type | Length | Value |
| --- | --- | --- |
| Defined in the specific TLVs, that use this format. | Variable | Value identifying the MIHF |

# 2.2. Proposed changes in section 8.5:

The proposed changes in IEEE P802.21/D05.00 are marked using the MS word revision marks.

- Message parameter TLV encoding

The following TLV encoding shall be used for parameters in MIH Protocol Messages. The Type field shall be one octet. The format of the Length field shall be per the “definite form” of ITU-T X.690.

Specifically, if the actual length of the Value field is less than or equal to 127 octets, then:

- The Length field shall occupy one octet

- The MSB of the Length field shall be set to 0, and

- The other 7 bits of the Length field shall be used to indicate the actual length of the Value field in octets.

If the length of the Value field is exactly 128 octets, then:

- The Length field shall occupy one octet

- The MSB of the Length field shall be set to the value '1', and

- The other seven bits of the Length field shall all be set to the value '0'.

If the length of the Value field is more than 127 octets, then:

- The Length field shall occupy more than one octet

- The MSB of the first octet of the Length field shall be set to 1.

- The other 7 bits of the first octet of the Length field shall be used to indicate the number of additional octets of the Length field (i.e., excluding the first octet), and

- The value of the remaining octets (i.e., excluding the first octet) of the Length field, when added to 128, shall be used to indicate the actual length of the Value field in octets.

TLV type values shall be unique. TLV encoding start at 1 and subsequent values are assigned in ascending order.

# TLV encoding

TLV fields and their associated Type codes are presented in Table X - TX.

| Table X - Type values for TLV encoding |
| --- |
| Type | Parameter name |
| 1 | MIH Event List |
| 2 | MIH Command List |
| 3 | MIIS Query Type List |
| 4 | Transport List |
| 5 | Register request code |
| 6 | Register validity period |
| 7 | Operation Status |
| 8 | Old Access Router MAC Address |
| 9 | New Access Router MAC Address |
| 10 | PoA MAC Address |
| 11 | Mobile Node MAC Address |
| 12 | Link Type |
| 13 | Link Identifier |
| 14 | Old Link Identifier |
| 15 | New Link Identifier |
| 16 | IP Renewal Flag |
| 17 | IP Address Configuration Methods List |
| 18 | Link Down Reason Code |
| 19 | Time Interval |
| 20 | Confidence Level |
| 21 | Link Going Down Reason |
| 22 | Unique Identifier |
| 23 | MIH Capability Flag |
| 24 | Link Parameter Type |
| 25 | Link Parameter Value |
| 26 | Threshold crossed |
| 27 | Link Parameter Report |
| 28 | Handover Type |
| 29 | Link Parameter List |
| 30 | Link Parameter Value List |
| 31 | Link Parameters Configuration Status List |
| 32 | Link Scan Response Sets |
| 33 | Link and PoA List |
| 34 | Handover Mode |
| 35 | Link Action |
| 36 | Handover Resource Query List |
| 37 | Handover Resource Response List |
| 38 | Handover Acknowledgement |
| 39 | IP Address |
| 40 | IP Address Information Status |
| 41 | Resource Status |
| 42 | Link Action Set |
| 43 | Action Result |
| 44 | Link Action Result |
| 45 | Handover Result |
| 46 | Resource Retention Status |
| 47 | Header TLV Source MIHF Identifier |
| 48 | Header TLV Destination MIHF Identifier |
| 49 | Header TLV Session Identifier |
| … TLVs related to MIH Information Service .. |

# 8.5.1. MIH event list

This parameter specifies a list of MIH events that may be carried in a message.

| Type | Length | Value |
| --- | --- | --- |
| 1 | 4 | Each MIH event is represented by a bit position in the 32-bit bitmap. When a bit is set to ‘1’, the corresponding MIH event is indicated: Bit 0: MIH_Link_Up Bit 1: MIH_Link_Down Bit 2: MIH_Link_Going_Down Bit 3: MIH_Link_Detected Bit 4: MIH_Link_Parameters_Report Bit 5: MIH_Link_Event_Rollback Bit 6: MIH_Link_PDU_Transmit_Status Bit 7: MIH_Link_Handover_Imminent Bit 8: MIH_Link_Handover_Complete Bit 9-31: (Reserved) |

# 8.5.2. MIH command list

This parameter specifies a list of MIH commands that may be carried in a message.

| Type | Length | Value |
| --- | --- | --- |
| 2 | 4 | The encoding uses the following bitmap where a bit set to 1 indicates that command(s) is indicated. Bit 0: MIH_Get_Link_Parameters Bit 1: MIH_Configure_Link Bit 2: MIH_Scan Bit 3: MIH_Net_HO_Candidate_Query MIH_Net_HO_Commit MIH_N2N_HO_Query_Resources MIH_N2N_HO_Complete Bit 4: MIH_MN_HO_Candidate_Query MIH_MN_HO_Commit MIH_MN_HO_Complete Bit 5-31: (Reserved) |

# 8.5.3. MIH query type list

This parameter specifies a list of MIIS query types that may be carried in a message.

| Type | Length | Value |
| --- | --- | --- |
| 3 | 1 | When a bit is set to ‘1’, the corresponding MIIS query type is indicated: Bit 0: TLV Bit 1: RDF_DATA Bit 2: RDF_SCHEMA_URL Bit 3: RDF_SCHEMA Bit 4~7: (Reserved) |

# 8.5.4. Transport option list

This parameter specifies the list of transport options for different MIH services.

| Type | Length | Value |
| --- | --- | --- |
| 4 | 4 | When a bit is set to ‘1’, the corresponding transport option is indicated: Bit 0: L2 for service management Bit 1: L3 or higher layer protocol for service management Bit 4: L2 for event service Bit 5: L3 or higher layer protocol for event service Bit 8: L2 for command service Bit 9: L3 or higher layer protocol for command service Bit 12: L2 for information service Bit 13: L3 or higher layer protocol for information service Other Bits: (Reserved) |

# 8.5.5. Register request code

This parameter specifies the Register Request Code.

| Type | Length | Value |
| --- | --- | --- |
| 5 | 1 | 0: Registration 1: Re-registration |

# 8.5.6. Register validity period

This parameter specifies the Register Validity Period.

| Type | Length | Value |
| --- | --- | --- |
| 6 | 4 | An integer indicating the time the registration is valid in seconds. |

# 8.5.7. Operation status

This parameter specifies the status of an operation.

| Type | Length | Value |
| --- | --- | --- |
| 7 | 1 | 0: Success 1: Unspecified Failure 2: Rejected 3: Authorization Failure 4: Network Error 5-255: (Reserved) |

# 8.5.8. Old Access Router MAC Address

This parameter TLV specifies a MAC Address for the old access router.

| Type | Format |
| --- | --- |
| 8 | MAC_ADDRESS |

# 8.5.9. New Access Router MAC Address

This parameter TLV specifies a MAC Address for the new access router.

| Type | Format |
| --- | --- |
| 9 | MAC_ADDRESS |

# 8.5.10. PoA MAC Address

This TLV specifies the MAC Address PoA.

| Type | Format |
| --- | --- |
| 10 | MAC_ADDRESS |

# 8.5.11. Mobile Node MAC Address

This TLV specifies the MAC Address for the mobile node.

| Type | Format |
| --- | --- |
| 11 | MAC_ADDRESS |

# 8.5.12. Link type

This TLV specifies the network type

| Type | Length | Value |
| --- | --- | --- |
| 12 | 8 | See table 9. |

# 8.5.13. Link identifier

This TLV specifies the current Link Identifier.

| Type | Format |
| --- | --- |
| 13 | LINK_ID |

# 8.5.14. Old link identifier

This TLV specifies the current Link Identifier.

| Type | Format |
| --- | --- |
| 14 | LINK_ID |

# 8.5.15. New link identifier

This TLV specifies the new Link Identifier.

| Type | Format |
| --- | --- |
| 15 | LINK_ID |

# 8.5.16 IP renewal flag

This parameter indicates whether an IP address renewal is required or not

| Type | Length | Value |
| --- | --- | --- |
| 16 | 1 | 0: Change in IP Address required 1: Change in IP Address NOT required 2-255: (Reserved) |

# 8.5.17. IP address configuration methods list

This parameter specifies the list of IP address configuration methods supported by a PoA.

| Type | Length | Value |
| --- | --- | --- |
| 17 | 4 | A 32-bit bitmap indicating the types of IP address configuration methods supported by a PoA: Bit 0: IPv4 static configuration Bit 1: IPv4 dynamic configuration (DHCPv4) Bit 2. Mobile IPv4 with FA (FA-CoA) Bit 3: Mobile IPv4 without FA (Co-located CoA) Bit 4~10: (Reserved for IPv4 address configuration) Bit 11: IPv6 stateless address configuration Bit 12: IPv6 stateful address configuration (DHCPv6) Bit 13: IPv6 manual configuration Bit 14: No configuration allowed Bit 15~31: (Reserved) |

# 8.5.18 Link down reason code

This parameter specifies the reasons for a Link Down indication.

| Type | Length | Value |
| --- | --- | --- |
| 18 | 1 | 0: EXPLICIT DISCONNECT 1: PACKET TIMEOUT 2: NO RESOURCE 3: NO BROADCAST 4: AUTHENTICATION FAILURE 5: BILLING FAILURE 6-127: (Reserved) 128-255: Vendor specific reason codes. See Table 34 for definition of the above reason codes. |

# 8.5.19. Time interval

This parameter specifies the duration of the time interval in milliseconds.

| Type | Length | Value |
| --- | --- | --- |
| 19 | 2 | Time interval in milliseconds |

# 8.5.20 Confidence level

This parameter specifies the confidence level as a percentage.

| Type | Length | Value |
| --- | --- | --- |
| 20 | 1 | Confidence level as a percentage (0-100) |

# 8.5.21 Link going down reason

This parameter specifies the reason code for a Link Going Down indication.

| Type | Length | Value |
| --- | --- | --- |
| 21 | 1 | 0: EXPLICIT DISCONNECT 1: LINK PARAMETER DEGRADING 2: LOW POWER 3: NO RESOURCE 4-127: (Reserved) 128-255: (Vendor specific reason codes) See Table 35 for definition of the above reason codes. |

# 8.5.22 Unique event identifier

This parameter specifies a unique identifier.

| Type | Length | Value |
| --- | --- | --- |
| 22 | 2 | An integer uniquely identifying a Link Going Down event. |

# 8.5.23 MIH capability flag

This parameter specifies the MIH Capability Flag.

| Type | Length | Value |
| --- | --- | --- |
| 23 | 1 | 0: MIH Capability NOT supported 1: MIH Capability Supported |

# 8.5.24. Link parameter type

This specifies the type of link parameter.

| Type | Length | Value |
| --- | --- | --- |
| 24 | 2 | First Octet: Type of link. 0: Generic link type 1-255: Link specific types as defined in Table 9. Second Octet: Subtype of Parameter Generic Link Parameters: 0: Number of supported CoS 1: Throughput 2: Packet Error Rate 3: Minimum Packet Transfer Delay 4: Average Packet Transfer Delay 5: Maximum Packet Transfer Delay 6: Packet Transfer Delay Jitter 7: Packet Loss Rate 8-255: Reserved [Editor's note: specific link parameter types TBD] |

# 8.5.25. Link parameter value

This specifies the current parameter value:

| Type | Length | Value |
| --- | --- | --- |
| 25 | Variable | The current value of the parameter. |

# 8.5.26. Threshold crossed

This specifies the threshold crossed by a link parameter:

| Type | Length | Value |
| --- | --- | --- |
| 26 | 1 | 0: Initiate Action Threshold crossed 1: Rollback Action Threshold crossed 2: Execute Action Threshold crossed |

# 8.5.27. Link parameter report

This parameter specifies a link parameter report.

| Type | Length | Value |
| --- | --- | --- |
| 27 | Variable | Consisting of the following TLVs - Parameter Type - Current Value - Threshold Crossed (optional) |

The embedded TLVs are defined as the follows:

Parameter Type:

| Type | Length | Value |
| --- | --- | --- |
| 24 | 1 | Parameter being reported, as defined in Table (Editor’s note: to be defined in assignment #4). |

Current Value:

| Type | Length | Value |
| --- | --- | --- |
| 25 | Variable | The current value of the parameter. |

Threshold Crossed:

| Type | Length | Value |
| --- | --- | --- |
| 26 | 1 | 0: Initiate Action Threshold crossed 1: Rollback Action Threshold crossed 2: Execute Action Threshold crossed |

# 8.5.28. Handover Type

This parameter specifies whether a handover is of intra-technology or inter-technology.

| Type | Length | Value |
| --- | --- | --- |
| 28 | 1 | 0: Intra-technology 1: Inter-technology |

# 8.5.29. Link parameters list

This parameter specifies a list of indicators of a set of link layer parameters for which certain action may be requested.

[Editor’s note: this needs to be re-worked into a structure of a list of indicators for media specific and generic link parameters].

| Type | Length | Value |
| --- | --- | --- |
| 29 | 4 | Set of link parameters for which status is requested Bit 0: Device Information Bit 1: Operation Mode Bit 2: Channel Identifier Bit 3: Battery Level Bit 4: Link QoS Parameters Type List (Editor’s note: to be fixed in assignment #4) Bit 5~31: Reserved |

# 8.5.30. Link parameters value list

[Editor’s note: this needs to be re-worked into a structure consisting of 1) a link ID, 2) a list of {type:value} for media specific and generic link parameters].

This parameter specifies a list of media specific and generic link parameters and their value of a link.

| Type | Length | Value |
| --- | --- | --- |
| 30 | Variable | a structure consisting of 1) a link ID, 2) a list of {type:value} for media specific and generic link parameters |

# 8.5.31. Link parameters configuration status list

[Editor’s note: this needs to be re-worked into a structure consisting of a list of {type:status} for media specific and generic link parameters].

This parameter specifies a list of media specific and generic link parameters and their configuration status of a link.

| Type | Length | Value |
| --- | --- | --- |
| 31 | Variable | a structure consisting of a list of {type:status} for media specific and generic link parameters |

# 8.5.32. Link scan response sets

[Editor’s note: this needs to be re-worked into a structure consisting of a list of {PoA ID:signal strength}].

This parameter specifies a list of PoAs and their signal strength.

| Type | Length | Value |
| --- | --- | --- |
| 32 | Variable | a structure consisting of a list of {PoA ID:signal strength} |

# 8.5.33. Link and PoAs list

This parameter specifies a link and a list of PoAs associated with the link type.

| Type | Length | Value |
| --- | --- | --- |
| 33 | Variable | Consisting of the following TLVs: - a link identifier TLV, and - one or more PoA MAC address TLVs. Note, each MAC Address is of the same length, since they belong to the same network type. |

The embedded TLVs are defined as the follows:

Link Identifier:

| Type | Format |
| --- | --- |
| 13 | LINK_ID |

PoA MAC Address:

| Type | Format |
| --- | --- |
| 11 | MAC_ADDRESS |

# 8.5.34. Handover mode

This parameter specifies whether a handover is of make-before-break or break-before-make.

| Type | Length | Value |
| --- | --- | --- |
| 34 | 1 | 0: Make-before-break 1: Break-before-make |

# 8.5.35. Link action

This parameter specifies the action to take on a link.

| Type | Length | Value |
| --- | --- | --- |
| 35 | 4 | Bit 0: LINK_DISCONNECT Bit 1: LINK_LOW_POWER Bit 2: LINK_POWER_DOWN Bit 3: LINK_NO_ACTION Bit 4: LINK_RESOURCE_RETAIN Bit 5: DATA_FORWARDING_REQUEST Bit 6: LINK_POWER_UP Bit 7-31: (Reserved) See 7.4.18.1.2 for description of the above link actions. Combination of actions is permissible. |

# 8.5.36. Handover resource query list

This parameter specifies a list of handover resources.

| Type | Length | Value |
| --- | --- | --- |
| 36 | 1 | Set of link parameters which may be queried for resources during handover: Bit 0: Maximum Bandwidth Bit 1-7: (Reserved) |

# 8.5.37. Handover resource response list

This parameter specifies the response due to query of resources

| Type | Length | Value |
| --- | --- | --- |
| 37 | Variable | List of values depending on the “Link resource parameters type” TLV ((Editor’s note: TBD), specified in that message. Currently only one Link resource parameter type (Maximum bandwidth) is defined, so this parameter will include a value for maximum bandwidth. |

# 8.5.38. Handover acknowledgement

This parameter specifies the status of a handover request.

| Type | Length | Value |
| --- | --- | --- |
| 38 | 1 | 0: Handover initiate 1: Handover abort |

# 8.5.39 IP address

This parameter specifies an IPv4 or IPv6 address.

| Type | Length | Value |
| --- | --- | --- |
| 39 | 4 or 16 | An IPv4 or IPv6 address. |

# 8.5.40. IP address information status

This parameter specifies the status of the IP address information request.

| Type | Length | Value |
| --- | --- | --- |
| 40 | 1 | 0: IP configuration Method is not available 1: DHCP Server address is not available 2: FA Address is not available 3: Access Router Address is not available 4: No information is provided due to accessibility of same entity (FA, Access Router, DHCP Server, etc) 5-255: (Reserved) |

# 8.5.41 Resource status

This parameter specifies the status of a handover resource.

| Type | Length | Value |
| --- | --- | --- |
| 41 | 1 | 0: Resource unavailable 1: Resource available |

# 8.5.42. Link action set

This parameter specifies a set of actions to be taken on a specific link.

| Type | Length | Value |
| --- | --- | --- |
| 42 | Variable | Consisting of the following TLVs: - a link identifier, - a set of actions to be taken on the link, and - execution time |

The embedded TLVs are defined as the follows:

Link Identifier:

| Type | Length | Format |
| --- | --- | --- |
| 13 | Variable | LINK_ID |

Link Action Set:

| Type | Length | Value |
| --- | --- | --- |
| 35 | 4 | Bit 0: LINK_DISCONNECT Bit 1: LINK_LOW_POWER Bit 2: LINK_POWER_DOWN Bit 3: LINK_NO_ACTION Bit 4: LINK_RESOURCE_RETAIN Bit 5: DATA_FORWARDING_REQUEST Bit 6: LINK_POWER_UP Bit 7-31: (Reserved) |

Time Interval:

This parameter specifies the execution time:

| Type | Length | Value |
| --- | --- | --- |
| 19 | 2 | Specifies the time elapsed before a link action needs to be taken. Value is expressed in ms and the range is from 0 to 10000. If Value = ‘0’, then the action is expected to be taken immediately. |

Comment:  Resuse Time Interval TLV definition, instead of Execution Time definition. Per this definition changed length to 2, this satisfies the maximum allowed value of 10,000.

# 8.5.43. Action result

This parameter specifies the link action result:

| Type | Length | Value |
| --- | --- | --- |
| 43 | 1 | 0 Resource Unavailable 1 Resource Busy 2 Resource Available 3 Abort Handover 4 Perform Handover 5-255 (Reserved) |

# 8.5.44. Link action result

This parameter specifies the result of a set of link action taken on a specific link.

| Type | Length | Value |
| --- | --- | --- |
| 44 | Variable | Consisting of the following TLVs: - a link identifier, - the result of the actions taken on the link |

The embedded TLVs are defined as the follows:

Link Identifier:

| Type | Length | Value |
| --- | --- | --- |
| 13 | Variable | (see 8.5.13. Link Identifier) |

Action Result:

| Type | Length | Value |
| --- | --- | --- |
| 43 | 1 | 0 Resource Unavailable 1 Resource Busy 2 Resource Available 3 Abort Handover 4 Perform Handover 5-255 (Reserved) |

# 8.5.45 Handover result

This parameter specifies the result of handover.

| Type | Length | Value |
| --- | --- | --- |
| 45 | 1 | 0: Success 1: Failure 2: Rejected |

# 8.5.46 Resource retention status

This parameter specifies the resource retention request.

| Type | Length | Value |
| --- | --- | --- |
| 46 | 1 | 0: Retain resources 1: Release resources |

# 8.5.47 Source Identifier

This specifies the Source Identifier for a MIH message.

| Type | TLV Name | Format |
| --- | --- | --- |
| 47 | Source Identifier | MIHF_ID |

# 8.5.48 Destination Identifier

This specifies the Destination MIHF ID for a MIH message.

| Type | TLV Name | Format |
| --- | --- | --- |
| 48 | Destination Identifier | MIHF_ID |

# 8.5.49 Session Identifier

This specifies the Session identifier.

| Type | Length | Value |
| --- | --- | --- |
| 49 | 4 | A unique identifier generated by the source and destination and is valid for a session |

…Definition of the Information Service TLVs …

- Link configure parameters type

This specifies a link parameter that may be configured for handover.

| Type | Length | Value |
| --- | --- | --- |
| Defined in messages | 1 | Type of link parameter to be configured. 0: Operation Mode 1: Link QoS Parameters List 2: Link Configure Parameter List (as defined in 7.3.3.1.2) 3-255: (Reserved) |

Comment: TLV not in used. Should it be deleted, or kept for specific used?

- MIH protocol messages

This subclause specifies different MIH protocol messages in TLV form. The shaded areas represent the MIH protocol header (including both fixed and optional header fields), while the unshaded areas represent the MIH protocol payload. The payload consists of a set of identifiers in TLV form.

All MIH messages carry MIHF ID TLVs for the Source and Destination Identifiers in the MIHF Variable Header part of the message.

- MIH messages for service management

- MIH_Capability_Discover request

If a requesting MIHF entity does not know the MIHF capable entity’s addresses, the requesting MIHF entity fills its source address field only and leaves the destination address blank and may broadcast this message. If a requesting MIHF entity knows the address of entity but does not know whether the entity is MIHF capable, this message is delivered to the entity in a unicast way.

This message contains the SupportedMihEventList, SupportedMihCommandList and SupportedISQueryTypeList parameters to enable  the receivng MIHF to recognize the sending MIHF's capability. Therefore, peer MIHF entities can recognize each other's MIH capablity by one MIH protocol message transaction.

MIH Header Fixed Fields (SID=1, Opcode=1, AID=1)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF ID)

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF ID )

SupportedMihEventList (TLV type=1; format see MIH Event List)

SupportedMihCommandList (TLV type=2; format see MIH Command List)

SupportedISQueryTypeList (TLV type=3; format see MIIS query type list)

SupportedTransportList (TLV type=4; format see Transport List)

- MIH_Capability_Discover response

This message may contain SupportedMihEventList, SupportedMihCommandList, SupportedISQueryTypeList, and SupportedTransportList in the MIH message data. Only an MIHF capable entity may receive the MIH_Capability_Discover response. Upon reception of an MIH_Capability_Discover response, the MIH_Capability_Discover confirm is transmitted. Destination addresses are copied from the MIH_Capability_Discover response and source addresses are filled with their addresses. An entity with an MIHF may also broadcast unsolicited MIH_Capability_Discover confirm message to advertise its MIH capability. [Editor’s note: need to re-write this]

MIH Header Fixed Fields (SID=1, Opcode=2, AID=1)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID)

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

SupportedMihEventList (TLV type=1; format see MIH event list)

SupportedMihCommandList (TLV type=2; format see MIH command list)

SupportedISQueryTypeList (TLV type=3; format see MIIS query type list)

SupportedTransportList (TLV type=4; format see Transport list)

Status (TLV type=7; format see Operation status)

- MIH_Register request

This message is transmitted to the remote MIHF to perform a registration or re-registration.

MIH Header Fixed Fields (SID=1, Opcode=1, AID=2)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

RequestCode (TLV type=5; format see Register request code)

- MIH_Register response

This message is sent in response to a registration or re-registration request.

MIH Header Fixed Fields (SID=1, Opcode=2, AID=2)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID)

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID.)

ValidityPeriod (TLV type=6; format see Register validity period)

Status (TLV type=7; format see Operation status)

- MIH_DeRegister request

This message is transmitted to the remote MIHF to request a de-registration. There is no parameter for this message.

MIH Header Fixed Fields (SID=1, Opcode=1, AID=3)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID)

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID)

- MIH_DeRegister response

This message is sent in response to a de-registration request.

MIH Header Fixed Fields (SID=1, Opcode=2, AID=3)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID)

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID)

Status (TLV type=7; format see Operation status)

- MIH_Event_Subscribe request

This message is sent by a remote MIHF (the subscriber) to subscribe to one or more event types from a particular event origination point.

MIH Header Fixed Fields (SID=1, Opcode=1, AID=4)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID)

LinkIdentifier (TLV type=13; format see LINK_ID)

RequestedMihEventList (TLV type=1; format see MIH event list)

- MIH_Event_Subscribe response

The response indicates which of the event types were successfully subscribed.

MIH Header Fixed Fields (SID=1, Opcode=2, AID=4)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see LINK_ID)

ResponseMihEventList (TLV type=1; format see MIH event list )

Status (TLV type=7; format see Operation status)

- MIH_Event_Unsubscribe request

This message is sent by a remote MIHF (the subscriber) to unsubscribe from a set of link layer events.

MIH Header Fixed Fields (SID=1, Opcode=1, AID=5)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see LINK_ID)

RequestedMihEventList (TLV type=1; format see MIH event list)

- MIH_Event_Unsubscribe response

The response indicates which of the event types were successfully unsubscribed.

MIH Header Fixed Fields (SID=1, Opcode=2, AID=5)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID)

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID)

LinkIdentifier (TLV type=13; format see LINK_ID )

ResponseMihEventList (TLV type=1; format see MIH event list)

Status (TLV type=7; format see Operation status)

- MIH messages for event service

- MIH_Link_Up indication

MIH Header Fixed Fields (SID=2, Opcode=3, AID=6)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see LINK_ID)

MacOldAccessRouter (optional) (TLV type=8; format see MAC_ADDRESS )

MacNewAccessRouter (TLV type=9; format see MAC_ADDRESS )

IPRenewalFlag (optional) (TLV type=16; format see IP renewal flag)

MobilityManagementSupport (optional) (TLV type=17; format see IP address configuration method list)

- MIH_Link_Down indication

This notification is delivered from an MIHF, when present in the PoA, to an MIHF in the network when a layer 2 connection is disconnected due to a certain reason with a mobile node.

MIH Header Fixed Fields (SID=2, Opcode=3, AID=7)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHD_IF )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF ID)

LinkIdentifier (TLV type=13; format see LINK_ID 8.5.13. Link Identifier)

MacOldAccessRouter (optional) (TLV type=8; format see Old Access Router MAC address)

LinkDownReasonCode (TLV type=18; format see 8.5.18 Link down reason code)

- MIH_Link_Going_Down indication

This message is transmitted to the remote MIHF when a layer 2 connectivity is expected (predicted) to go down within a certain time interval.

MIH Header Fixed Fields (SID=2, Opcode=3, AID=8)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

TimeInterval (TLV type=19; format see 8.5.19 Time interval)

ConfidenceLevel (TLV type=20; format see 8.5.20 Confidence level)

LinkGoingDownReason (TLV type=21; format see 8.5.21 Link going down reason)

UniqueEventIdentifier (TLV type=22; format see 8.5.22 Unique event identifier)

- MIH_Link_Event_Rollback indication

This message is used in conjunction with Link_Going_Down. If the link is no longer expected to go down in the specified time interval, a Link_Event_Rollback message is sent to the remote Event destination.

MIH Header Fixed Fields (SID=2, Opcode=3, AID=11)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID)

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see LINK_ID )

UniqueEventIdentifier (TLV type=22; format see 8.5.22 Unique event identifier)

- MIH_Link_Detected indication

This message is transmitted to the remote MIHF when a new link has been detected.

MIH Header Fixed Fields (SID=2, Opcode=3, AID=9)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID)

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see LINK_ID)

MIHCapabilityFlag (TLV type=23; format see 8.5.23 MIH capability flag)

- MIH_Link_Parameters_Report indication

This message indicates changes in link parameters that have crossed pre-configured threshold levels.

MIH Header Fixed Fields (SID=2, Opcode=3, AID=10)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

LinkParameterReport 1 (TLV type=27; format see 8.5.27. Link parameter report)

...

LinkParameterReport k (TLV type=27; format see 8.5.27. Link parameter report)

- MIH_Link_Handover_Imminent indication

This message indicates that a link layer handover decision has been made and its execution is imminent.

MIH Header Fixed Fields (SID=2, Opcode=3, AID=12)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

OldLinkIdentifier (TLV type=14; format see LINK_ID )

NewLinkIdentifier (TLV type=15; format see LINK_ID )

HandoverType (TLV type=28; format see 8.5.28.Handover Type)

MacOldAccessRouter (optional) (TLV type=8; format see MAC_ADDRESS )

MacNewAccessRouter (optional) (TLV type=9; format see MAC_ADDRESS )

- MIH_Link_Handover_Complete indication

This message indicates that a link layer handover has been completed.

MIH Header Fixed Fields (SID=2, Opcode=3, AID=13)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

OldLinkIdentifier (TLV type=14; format see LINK_ID )

NewLinkIdentifier (TLV type=15; format see LINK_ID )

MacOldAccessRouter (TLV type=8; format see MAC_ADDRESS )

MacNewAccessRouter (TLV type=9; format see MAC_ADDRESS )

- MIH messages for command service

- MIH_Get_Link_Parameters request

This message is used to discover the status of currently available links.

MIH Header Fixed Fields (SID=3, Opcode=1, AID=14)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier 1 (TLV type=13; format see 8.5.13. Link Identifier)

...

LinkIdentifier k (TLV type=13; format see 8.5.13. Link Identifier)

GetStatusRequestSet (TLV type=29; format see 8.5.29. Link parameters list)

- MIH_Get_Link_Parameters response

This message is used by an MIHF to report the status of currently available links.

MIH Header Fixed Fields (SID=3, Opcode=2, AID=14)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

GetStatusResponsetSet 1 (TLV type=29; format see Link parameters value list)

...

GetStatusResponsetSet k (TLV type=29; format see Link parameters value list)

Status (TLV type=7; format see Operation status)

- MIH_Configure_Link request

This message is used to configure the link and control the link behavior.

MIH Header Fixed Fields (SID=3, Opcode=1, AID=16)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see LINK_ID ) ((Editor’s note: may not needed if ConfigureRequestSet def already contains link ID)

ConfigureRequestSet (TLV type=29; format see Link parameters value list)

- MIH_Configure_Link response

This message returns the status of a configuration request.

MIH Header Fixed Fields (SID=3, Opcode=2, AID=16)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see LINK_ID )

ConfigurationResponseList (TLV type=31; format see 8.5.31. Link parameters configuration status list)

Status (TLV type=7; format see Operation status)

- MIH_Scan request

This message is used to scan a list of PoAs for a specific link type.

MIH Header Fixed Fields (SID=3, Opcode=1, AID=17)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

ScanLinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

- MIH_Scan response

This message returns the list of PoAs and their respective signal strength for a specific link type after a scan operation.

MIH Header Fixed Fields (SID=3, Opcode=2, AID=17)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

ScanLinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

ScanResponseSets (TLV type=32; format see 8.5.32. Link scan response sets)

Status (TLV type=7; format see Operation status)

- MIH_Net_HO_Candidate_Query request

This message is used for communication between the MIHF on an MN with the MIHF on a network. The function is used to communicate an intent of network initiated handover.

MIH Header Fixed Fields (SID=3, Opcode=1, AID=18)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

SuggestedNewLink 1 (TLV type=33; format see 8.5.33. Link and PoAs list)

...

SuggestedNewLink k (TLV type=33; format see 8.5.33. Link and PoAs list)

HandoverMode (TLV type=34; format see 8.5.34. Handover mode)

OldLinkAction (TLV type=35; format see 8.5.35. Link action)

QueryResourceList (TLV type=36; format see 8.5.36. Handover resource query list)

- MIH_Net_HO_Candidate_Query response

This message is used for communication between the MIHF on an MN with the MIHF on network. The function is used to respond to an intent of network initiated handover.

MIH Header Fixed Fields (SID=3, Opcode=2, AID=18)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

CurrentLinkIdentifier (TLV type=13; format see LINK_ID)

HandoverAck (TLV type=38; format see 8.5.38Handover acknowledgment)

PreferredLink 1 (TLV type=33; format see 8.5.33. Link and PoAs list)

...

PreferredLink k (TLV type=33; format see 8.5.33. Link and PoAs list)

RequestedResourceSet (TLV type=37; format see 8.5.37. Handover resource response list)

Status ((Editor’s note: same as the Error Code?) (TLV type=7; format see Operation status)

- MIH_MN_HO_Candidate_Query request

MIH Header Fixed Fields (SID=3, Opcode=1, AID=19)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

CurrentLinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

CandidateLink 1 (TLV type=33; format see 8.5.33. Link and PoAs list)

...

CandidateLink k (TLV type=33; format see 8.5.33. Link and PoAs list)

QueryResourceList (TLV type=36; format see 8.5.36. Handover resource query list)

IPConfigurationMethods (TLV type=17; format see 8.5.17 IP address configuration methods list )

ServingFAAddress¦ServingAccessRouterAddress¦DHCPServerAddress (TLV type=39; format see 8.5.39 IP address)

- MIH_MN_HO_Candidate_Query response

MIH Header Fixed Fields (SID=3, Opcode=2, AID=19)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

CurrentLinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

PreferredCandidateLink 1 (TLV type=33; format see 8.5.33. Link and PoAs list)

...

PreferredCandidateLink k (TLV type=33; format see 8.5.33. Link and PoAs list)

AvailableResourceSet (TLV type=37; format see 8.5.37. Handover resource response list)

IPConfigurationMethods (TLV type=17; format see 8.5.17 IP address configuration methods list )

ServingFAAddress¦ServingAccessRouterAddress¦DHCPServerAddress (TLV type=39; format see 8.5.39 IP address)

IPAddressInformationStatus (TLV type=40; format see 8.5.40 IP address information status)

Status (TLV type=7; format see Operation status)

- MIH_N2N_HO_Query_Resources request

This message is used by the MIHF on the serving network to communicate with its peer MIHF on the candidate network. This is used to prepare the new link resource for impending handover and to query the available link resource of the candidate network. This message is also used to achieve IP address related information on the candidate network.

MIH Header Fixed Fields (SID=3, Opcode=1, AID=20)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID MIHF ID)

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID)

QueryResourceList (TLV type=36; format see 8.5.36. Handover resource query list)

IPConfigurationMethods (TLV type=17; format see 8.5.17 IP address configuration methods list )

ServingFAAddress¦ServingAccessRouterAddress¦DHCPServerAddress (TLV type=39; format see 8.5.39 IP address)

- MIH_N2N_HO_Query_Resources response

This message is used by an MIHF on the candidate network to communicate with its peer MIHF on the serving network. This is used to return the result of resource preparation of the impending handover and to notify the MIHF on the serving network of the link resource status and IP address related information of the candidate network.

MIH Header Fixed Fields (SID=3, Opcode=2, AID=20)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

ResourceStatus (TLV type=41; format see 8.5.41 Resource status) ((Editor’s note: can this be merged into Status?)

AvailableResourceSet (TLV type=37; format see 8.5.37. Handover resource response list)

IPConfigurationMethods (TLV type=17; format see 8.5.17 IP address configuration methods list )

ServingFAAddress¦ServingAccessRouterAddress¦DHCPServerAddress (TLV type=39; format see 8.5.39 IP address)

IPAddressInformationStatus (TLV type=40; format see 8.5.40 IP address information status)

Status (TLV type=7; format see Operation status)

- MIH_Net_HO_Commit request

This message is used by the MIHF to communicate the intent to commit to a handover request to a specific link and PoA.

MIH Header Fixed Fields (SID=3, Opcode=1, AID=21)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID MIHF ID)

LinkActionSet 1 (TLV type=42 format see Link action set )

...

LinkActionSet k (TLV type=42; format see Link action set )

- MIH_Net_HO_Commit response

This message is used by the MIHF to communicate the response of request to commit to a handover request to a specific link and PoA.

MIH Header Fixed Fields (SID=3, Opcode=2, AID=21)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkActionResult 1 (TLV type=44; format see 8.5.44 Link action result)

...

LinkActionResult k (TLV type=44; format see 8.5.44 Link action result)

Status (TLV type=7; format see Operation status)

- MIH_MN_HO_Commit request

MIH Header Fixed Fields (SID=3, Opcode=1, AID=22)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

CurrentLinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

NewLinkIdentifier (TLV type=15; format see 8.5.13. Link Identifier)

TargetPoA (TLV type=10; format see MAC_ADDRESS )

OldLinkActions (TLV type=35; format see 8.5.35. Link action)

- MIH_MN_HO_Commit response

MIH Header Fixed Fields (SID=3, Opcode=2, AID=22)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

CurrentLinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

Status (TLV type=7; format see Operation status)

- MIH_MN_HO_Complete request

MIH Header Fixed Fields (SID=3, Opcode=1, AID=23)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

HandoverResult (TLV type=45; format see 8.5.45 Handover result)

- MIH_MN_HO_Complete response

MIH Header Fixed Fields (SID=3, Opcode=2, AID=23)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

LinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

Status (TLV type=7; format see Operation status)

- MIH_N2N_HO_Complete request

This message is used by the MIHF to communicate the status of handover operation.

MIH Header Fixed Fields (SID=3, Opcode=1, AID=24)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

HandoverResult (TLV type=45; format see 8.5.45 Handover result)

- MIH_N2N_HO_Complete response

This message is used by the MIHF to communicate the response following the completion of the handover operation. The message is used to communicate the preferred action to be taken w.r.t resources associated with the previous connection. If the handover is successful, the resources may be released.

MIH Header Fixed Fields (SID=3, Opcode=2, AID=24)

Source Identifier = sending MIHF ID (TLV type=47, format see MIHF_ID )

Destination Identifier = receiving MIHF ID (TLV type=48, format see MIHF_ID )

CurrentLinkIdentifier (TLV type=13; format see 8.5.13. Link Identifier)

ResourceRetainStatus (TLV type=46; format see 8.5.46 Resource retention status)

Status (TLV type=7; format see Operation status)

# Annex A: List of MIH Messages using MAC_ADDRESS TLV Types.

List of MIH Messages using MacOldAccessRouter/ MacNewAccessRouter TLVs

Link Up indication

Link down Indication

MIH_Link_Handover_Imminent indication

MIH_Link_Handover_Complete indication

List of MIH Messages using TargetPoA TLV

MIH_MN_HO_Commit request

# Annex B: List of MIH Messages using LINK_ID TLV Types.

List of MIH Messages using Link Identifier TLV

Link Up Indication

Link Down Indication

MIH_Get_Link_Parameters request

MIH_Configure_Link request

MIH_Configure_Link response

MIH_Scan request

MIH_Scan response

MIH_Net_HO_Candidate_Query response

MIH_MN_HO_Candidate_Query request

MIH_MN_HO_Candidate_Query response

MIH_MN_HO_Commit request

MIH_MN_HO_Commit response

MIH_MN_HO_Complete request

MIH_MN_HO_Complete response

MIH_N2N_HO_Complete response

MIH_N2N_HO_Complete response

List of MIH Messages using New/Old LinkIndentifier TLVs

MIH_MN_HO_Commit request

MIH_Link_Handover_Imminent indication

MIH_Link_Handover_Complete indication

# Footnotes

Note that the TLV Type field length is different than the Information Element Type length, which is 4 octets.