## Slide 1: Proposal for IEEE 802.21 solution
eric.njedjou@francetelecom.com

## Slide 2: Outline
Needed modifications to the Requirements Document
Components of the Solution
MIH Architecture
Event Indication
Information Service
Discuss endorsement of changes to the Requirement Document

## Slide 3: Needed modifications to the Requirements Document
Section 2: Definitions
  Network Selection:
    Current: the process by which a mobile terminal collects appropriate information and select an L2 link for higher layer communication is called Network Selection
    Required for the sake of being policy agnostic: the process by which a mobile terminal or an entity within the network collects appropriate information and selects an L2 link for higher layer communication is called Network selection

## Slide 4: Required modifications to the Requirements Document
Section 4: Architecture
  Section 4.1: Intended handover function should be everything but Media Independant!
  Reason:the handover decision making process should take into account the diversity of attributes between links to perform the best selection
  Suggestion: Change from Media Independent (MIH) to Heterogeneous Media Handover (HMH)

## Slide 5: Required Modifications to the Requirements Document
Section 4: Architecture
  MIH function is intended to provide services at network mobility and applications layers.
  MIH function is also intended to request services from link layers via appropriate SAPs
  This defines a layer
  Actually what has to be standardized within 802.21 is;
    An Heterogeneous/Inter Media Convergence (HMC/IMC) Layer
      Requires time and hard work!
  The Heterogeneous Media Handover function specification should be let at the discretion of Equipment vendors and Operators
    Standardized parameters to achieve that function should be available though

## Slide 6: Components of the solution
Architecture
  MIH function
  Event indication
  Information service
Handover scenarios addressed
  A single 802.11 interface going across ESS (in Phase 1 proposal)
  Handover between UMTS and 802.11 interfaces
Technologies affected by the proposal
  Couple of GPRS/UMTS Specifications in Release 6
  IEEE Std 802.11-1999, IEEE Draft 802.11i-2004, IEEE Draft 802.11e-2003

## Slide 7: HMH Architecture
Multi Access Mobile Station

## Slide 8: HMC layer at UMTS side
Architecture placement in protocol stack
  To be eventually figured out by 3GPP!
  Requests from IEEE 802.21 are to be adressed to 3GPP according to;
    Requirements on;
      QoS attributes mapping between technologies
      Security attributes mapping between technologies
      ….
    Need to provide services to upper layers as an L3MP

## Slide 9: HMC layer at UMTS side
Architecture placement in protocol stack on station/network
  Request from 802.21 of services to HMC layer;
    From GMM/SM, that performs
      Attachment to the UMTS network
      Mobility Management states handling
      Procedures to activate, deactivate and
        Modify a PDP context
    From RRC, that performs
      Station measurements reporting
      Radio Resources Management
      Requested QoS control
      Paging control
      Initial cell selection/re-selection in idle mode
      …
GMM/SM
RRC
RLC
MAC
LI
UMTS Control plane protocol stack
HMC

## Slide 10: HMH function at UMTS side
Depending on the coupling model
  the importance of the HMH function between terminal and network side will vary
  The HMC entity at terminal side will be able to connect to its network peer or not
  Standard should be coupling type agnostic!
    General cases will be describred here

## Slide 11: HMC layer at 802.11 side
Architecture placement in protocol stack
  To be figured out by IEEE 802.11 Project Task Groups!
  Requests from IEEE 802.21 are to be addressed to IEEE 802.11 according to;
    Requirements;
      On QoS attributes mapping between technologies
      On Security attributes mapping between technologies
      …
    Need to provide services to upper layers as an L3MP

## Slide 12: HMC layer at 802.11 side
Architecture placement in protocol stack on station
  Request from 802.21 of services to the HMC layer
    From 802.11 MAC, that performs
      Association/Re-association functions
      QoS provisionning (defined by 11e)
      Security functions as part of 11i exchange
    From 802.11 PHY, that provides
      Station Measurements of Signal Strength
        and Quality
LLC
MAC
PHY
802.11 STA
HMC

## Slide 13: HMC Messages
Functions
  Establishment/Release of the Heterogeneous Media Convergence connection between HMC peers (station and network)
  Request for handover to a particular link (for instance coming from applications and relayed to the HMH function in the network)
    Such a request would be also locally adressed (within the HMH function in the terminal)
  Instruction to Mobility layers to switch data flows between links according to the handover decision made in the HMH function
  Acknowledgement of the handover completion to HMC peer in the network

## Slide 14: HMH interaction with upper layers
Important 802.21 requirement
  Higher layer mobility protocols shall be supported
Interface between an L3MP and the HMH function:
  HMC messages arrived from the network should be formatted for use for example by the Mobile IP layer for care-of address re-selection
    Effort for IETF recommendations document will have to be initiated
Interface between Applications and the MIH function
  Applications should be able to generate handover requests messages to the HMH function: these resquests would be either processed locally or sent to the network
    Implementation specific

## Slide 15: HMC Messages
Semantics
  To be determined during protocol design phase

## Slide 16: Transport for HMC messages
3GPP
  RRC (UMTS)
    Needed extensions to be defined
  LLC (GPRS)
    Needed extensions to be defined
IEEE 802.11
  MAC
    Define Heterogeneous Media subtype of the Management frame

## Slide 17: Event Indication to HMC
3GPP station at station/network side
  UMTS station has attached to the network (GMM/SM layer)
    Station_attached (station/SGSN to HMC layer, cell an routeing area identity, ciphering algorithm used)
    Effect on receipt:
    Recipient: local
  UMTS station has detached from the network (GMM/SM layer)
  Station_detached (station/SGSN to HMC layer, reason)
    Effect on receipt:
    Recipient: local

## Slide 18: Event Indication to HMC
3GPP at station/network side
  Change in the Mobility Management state (GMM/SM layer)
    Mobility_Management_State_Changed (station/SGSN to HMC layer, precedent MM state, new MM state)
    Effect on receipt:
    Recipient: local
  PDP context has been activated (GMM/SM layer)
    PDPcontext_is_activated (station/SGSN to HMC layer, PDP type, PDP state, QoS profile requested, QoS profile negotiated, APN)
    Effect on receipt:
    Recipient: local

## Slide 19: Event Indication to HMC
3GPP at station/network side
  PDP context has been modified (GMM/SM layer)
    PDPcontext_is_modified (station/SGSN to HMC layer, PDP type, PDP state, QoS profile requested, new QoS profile negotiated, APN)
    Effect on receipt:
    Recipient: local
  PDP context has been deactivated
    PDPcontext_is_deactivated (station/SGSN to HMC layer, PDP type, PDP state, QoS profile requested, new QoS profile negotiated, APN)
    Effect on receipt:
    Recipient: local

## Slide 20: Event Indication to HMC
3GPP at station/network side
  Physical Layer Measurement report available (RRC layer)
    Measurement_report_available (station/RNC to HMC layer, report)
    Effect on receipt:
    Recipient: local
IEEE 802.11 at station side
  Received Signal Strentgh Indicator value reaches low threshold (PHY layer)
    RSSI_reaches_low_thresold(station to HMC layer in network)
    Effect on receipt:
    Recipient local/remote

## Slide 21: Event Indication to HMC
IEEE 802.11 at network side (optionally 11e/11i compliant)
  STA has associated to an Access Point
    Station_associated (station/network to HMC layer, BSSID of AP, SSID, RSN Elements)
    Effect on receipt:
    Recipient: local
  STA has deassociated
    Signal the event to the HMC layer
    Station_deassociated (station/network to HMC layer, reason)
    Effect on receipt:
    Recipient: local
We may want event indication also from 11k, 11u, WNM whose standards are not yet available!

## Slide 22: Event Indication to HMC
IEEE 802.11 at station side
  Received Signal Quality Indicator value reaches low threshold (PHY layer)
    RSQI_reaches_low_thresold(station to HMC layer in network)
    Effect on receipt:
    Recipient:remote HMC layer
EEE 802.11e at network side
  QoS BSS load information reaches high threshold
    QoSBSS_load_reaches_high_thresold (network to HMC layer, BSSID of AP)
    Effect on receipt:
    Recipient: local HMC layer

## Slide 23: Event Indication to the HMH function
The HMC layer receives event indications from specific link layers technologies
It transcodes them into abstracted events parameters to be used by the HMH function in the handover decision making process
The HMC layer relays the formatted event indications to HMH through an event service to be defined
Higher Layer Mobility Protocols will be consumers of the HMH function provided information
HMH function messages to Higher Layer Mobility Protocols are implemention specific

## Slide 24: Information Service
Station:
  Preferred access links/networks for the station (link type with provider IDs -PLMN/SSIDs list)
  Barred access networks (associated provider IDs -PLMN/SSIDs list)
  Level of QoS required by different applications
  Subscription type (roaming profile, billing ability…)
  ....
Network:
  Characteristics of the radio access network at particular locations (cell size and capacity, Access Point capabilities…)
  preferred and/or forbidden SSID/PLMN list