## Slide 1: Discussion Item for 802.21 Morning Teleconference (Rev .01)

## Slide 2
Media Independent Handover Proposal Scope Matrix for Discussion Part I

## Slide 3
Media Independent Handover Proposal Scope Matrix for Discussion Part II
For a Proposal to be considered a FULL PROPOSAL at least one entry in each row must be set to “SUPPORTED”

## Slide 4: Media Independent Handover Call Flow Template for discussion
Old Point of Attachment
Multimode STA
New Point of Attachment
HL
MIH Function
LL
LL
HL
MIH Function
LL
HL
MIH Function
Local Triggers
Local Triggers
Remote Triggers
Description of MIH Actions /Processing if any
Establishment and Release of Old/New Resources Description
Notes: 1.) Shows an 802.X session in progress – a rough view of the data path is shown
2.) 802.3 PHY is detected I.E. the combo Station is plugged in
3.) Results in a MIH_PHY_EVENT sent to the MIH function
4.) A decision is made by some policy function to begin a handover
5.) MIH enters the HO Prepare State
6.) The “Make” process is started by sending a MIH_HO_PREPARE trigger to the HL
7.) This trigger contains routing info that the MIH function collected when it first accessed the system. This facilitates the acquisition of the new CoA.
8.) Similarly, HO_PREPARE is sent to prepare the new LL entity
9.) A new IP tunnel is established
10.) This example assumes “Multiple CoA registration” so at this point two IP streams are in place.

## Slide 5
Proposed Minimum Set of Call Flow Scenarios for discussion (FULL PROPOSAL)