## Slide 1: CARD Protocol for 802.21 Information Service
July 18, 2005
Ajoy Singh (Motorola)
Marco Liebsch (NEC Europe)

## Slide 2: Candidate Access Router Discovery Protocol Overview
CAR: Candidate Access Router (access routers of neighboring cells) or neighboring access routers
CARD: Candidate Access Router Discovery
CARD Protocol in IETF: RFC 4066
Basic functionality
  Collect and distribute information about the (wireless) access network, in particular, information about the current and neighboring access routers and access points (base stations).
  Information is distributed from the CARD network entity (assumed to be located in access routers) to the mobile nodes.
Information distribution modes
  Request/Reply (Solicited) Mode
  Broadcast or multicast (Unsolicited) Mode
Requirements considered for CARD
  Can translate L2 address of a neighboring access point to the IP address of the CAR (i.e., candidate NAR).
    Access point can be separate from CAR.
  Enables obtaining of information about the relevant information (called capabilities) of CAR.
    E.g., access point channel numbers, access router load, …
  Must support inter-technology handovers.
  Should avoid unnecessary transmissions to MN.
  Must not depend on any particular mobility management protocol.
  Must work with variable topology

## Slide 3: Candidate Access Router Discovery Protocol Overview
Possible applications
  Fast handoff (seamless handoff)
  Load balancing between ARs.
  Bandwidth-intensive applications.
  Minimization of cost.
  Inter-technology handovers.
  Adaptability to changing topology without Ad hoc routing schemes.
CARD messages
  Defined for AR (CARD network entity) <-> Mobile Node
    Use ICMP for transport
  Defined for (CARD network entity) <-> AR (CARD network entity)
    Use SCTP or UDP for transport
  Information query options
    Preferences: same as filters (specify what type of information is needed) (eg. I am interested in Link Type.)
    Requirements : specify the conditions which are information types and required values (eg. Link type should be 802.11.)

## Slide 4: Proposal to 802.21
IP-based protocol is a good alternative solution for IEEE 802.21 Information Service (IS) for Media Independent Handoff.
  Can be used where MAC layer changes is difficult to make?
  Media independent by definition
  Easy to implement and deploy
  Flexible location of information source
Existing IETF protocols should be investigated with respect to IS requirements.
CARD is the primary candidate IETF protocol to be considered for IS.
  Basically same target functionality.
  Output of 4 years of IETF work and already published as RFC.
AR is a physical entity. CARD network entity can be separate from AR.
Extensions or modification of CARD to meet IS requirements is possible.
  New RFC (standard track) for revised CARD can be pursued.