## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-05-0326-01-0000
Title: IS Scenario
Date Submitted: July 28, 2005
Presented at IEEE 802.21 session #10 in Garden Grove, CA
Authors or Source(s):
Peretz Feder, Andrea Francini
Abstract: Information Service scenario and initial requirements for an IS protocol

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3: Communication Model for IS
IS Functional Entities
  Network MIHF Instance (NMI)
    Resides in MIH-enabled network element
    Network element must be Layer-4 capable
  Mobile MIHF Instance (MMI)
    Resides in Mobile Node
  IS Server (ISS)
    IS Information Element repository
IS Reference Points
  ISc: between NMI and ISS
    Relies on L3/4 transport
    NMI must reside in L3/4-capable network element
  ISd: between MMI and ISS
    Relies on L3/4 transport

## Slide 4: IS Protocol Features
IS protocol defines exchanges over ISc and ISd
  ISc mostly conveys:
    Requested Information Elements from ISS to NMI (e.g., for network-initiated handovers)
  ISd mostly conveys:
    Requested Information Elements from IIS to MMI (e.g., for mobile-initiated handovers)
IS protocol relies on L3/4 transport
  No L2 transport since no reference point explicitly maps onto access link
IS protocol requirements
  Protocol messages carry Information Elements specified in 802.21
  Protocol defines message format and message payload
  Protocol exchanges are query-based (request/response)
  Protocol provides for IS server discovery
  Protocol provides for mutual authentication between functional entities
  Protocol provides for optional payload encryption

## Slide 5: Proxy and Relay ISS Option
IS Caching - Additional IS Functionality
  Network MIHF Instance (NMI) Relay
    Caching IS elements from IS server
    No need to access IS server with every transaction
    A new reference point?
IS Reference Points
  ISy: between MMI and ISS (relay)
    Relies on L3/4 transport
  ISx: between ISS (proxy) and ISS
    Relies on L3/4 transport