## Slide 1
This document specifies how MAC management frames of IEEE 802.16e can be mapped to the link layer events that are described in P802-21-D00-01.pdf.

## Slide 2: IEEE 802.16e MAC Management Frames
MOB_MSHO-REQ
  The MS may transmit an MOB-_MSHO-REQ message when it wants to initiate an HO.
MOB_BSHO-REQ
  The BS may transmit a MOB_BSHO-REQ message when it wants to initiate an HO.
MOB_BSHO-RSP
  The BS shall transmit an MOB_BSHO-RSP message upon reception of MOB_MSHO-REQ message.
MOB_HO-IND
  An MS shall transmit a MOB_HO-IND message for final indication that it is about to perform a HO.
  0b00 : serving BS release
REG-RSP
  For mobile subscribers in normal operation, when the information is available to create CID update TLV, the target BS shall include the CID_update and SAID_update TLVs in the REG-RSP for an MS recognized by the target BS as performing HO or Network Re-entry from Idle Mode.

## Slide 3: MSS initiated
Network initiated
L2 Handover in IEEE 802.16e

## Slide 4: Link Layer Events Mapping
Link UP
  REG-RSP
Link Handoff Imminent
  MOB_HO-IND
Link Going Down
  MSS initiated handover
    MOB_BSHO-RES or MOB_BS-HO-REQ
  Network initiated handover
    MOB_BS-REQ or MOB_BSHO-RES