## Slide 1: 802.16g Primitives for HO (BS side only)
HO request
  This primitive is used by a serving BS to inform the mobility control entity in NCMS of an HO request from an MSS
HO indication
  This primitive is used by the mobility control entity in NCMS to inform target BSes of the pending HO.
HO response
  The mobility control entity in NCMS responds to the serving BS with the list of recommended target BSes.
HO confirmation
  This primitive is used by the target BS to reponds to the HO indicaion primitive from the serving BS or the mobility control entity in NCMS.
HO start
  In case of HO, this primitive is used to indicate the starting of the actual HO.
HO cancel
  In case of HO, this primitive indicates the cancellation of the pending HO.
HO directive
  This primitive is generated by the mobility control entity in NCMS to induce the handover of a particular MSS. Transmission of MOB_BSHO-REQ message is triggered by this primitive.

## Slide 2: Examples of 802.16g HO primitives

## Slide 3: .16g Query MAC Management Messages
Query IE Request (QRY_IE_REQ)
  BS uses the QRY_IE_REQ message to query information on the SS by describing by one or more IEs. The QRY_IE_REQ message is sent from the BS to the SS on the SS’s primary management connection.
Query IE Response (QRY_IE_RSP)
  The QRY_IE_RSP message is sent by the SS in response to QRY_IE_REQ containing the results of the information elements sent in the corresponding QRY_IE_REQ. The QRY_IE_RSP message is sent from the SS to the BS on the SS’s primary management CID.
Set IE Request (SET_IE_REQ)
Set IE Response (SET_IE_RSP)
* IEs are left as TBD in the .16g baseline document

## Slide 4: 802.16 Primitive example (Scanning)

## Slide 5: .16 MAC Management messages for MIH
Syntax | Length | Description
MOB_MSMIH-REQ_Message_Format( ) { |  | 
Management Message Type = xx | 8bits | 
TLV Encoded Information | variable | Specific TLV
} |  | 
Syntax | Length | Description
MOB_MSMIH-RSP_Message_Format( ) { |  | 
Management Message Type = xx | 8bits | 
TLV Encoded Information | variable | Specific TLV
} |  | 
Syntax | Length | Description
MOB_BSMIH-REQ_Message_Format( ) { |  | 
Management Message Type = xx | 8bits | 
TLV Encoded Information | variable | Specific TLV
} |  | 
Syntax | Length | Description
MOB_BSMIH-RSP_Message_Format( ) { |  | 
Management Message Type = xx | 8bits | 
TLV Encoded Information | variable | Specific TLV
} |  | 

## Slide 6: L2 requirements for 802.16
Protocol Architecture
Primitives
  Primitives in MS
  Primitives in BS
    Primitives for inside BS
    Primitives for Inter PoA Communication (Ib)
      Most primitives in the 802.16g baseline document fall into this category
      Dependency with 802.21WG about Ib
MIH Capability Delivery through broadcast message (DL-MAP) like beacon in 802.11
  What kind of information should be delivered?
    Information should be as small as possible
Neighbor advertisement extension
  What kind of .21 specific information should be included?
Remote MIH Message delivery
  Control Plane (with Basic CID)
    MAC management messages
  Data Plane
    CS extension