## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-05-0300-03-0000
Title: Proposed 802.21 Presentation for 3GPP
Date Submitted: August, 11th, 2005
Presented at first 802.21-3GPP Teleconference
Authors or Source(s): Ulises Olvera, Alan Carlton
Abstract:
Provide 3GPP community with a high lever description of the -802.21 specification

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3
Motivation
Main Goals:
  Aid 3GPP in the realization of Interworking Scenario 4 and 5 (ref.TR 22.934)
  Ensure that 802.21 requirements be considered within other standard bodies
  Update relevant 3GPP groups with latest development in 802.21 standards

## Slide 4
MIH Model

## Slide 5
Current 802.21 Scope
Current Draft defines:
  Media Independent Handover Principles and Design Assumptions
  Supported Media Independent Services
  Service Access Points and their Primitives
  A Media Independent Handover Protocol

## Slide 6
MIH Principles
MIH Principles Dos:
  802.21 specifies procedures that aid in the handover decision making, providing ling layer state information to MIH users.
  802.21 specifies procedures that aid in the provisioning of network information and the basic content of the this information
  802.21 specifies command procedures that allow service continuity across heterogeneous networks
MIH Principles Don’ts
  802.21 neither controls handover selection nor defines handover policies
  802.21 neither controls network detection nor specifies network selection procedures nor network information provisioning

## Slide 7
Design Assumptions
Design Assumptions Dos:
  802.21 cross-layer entity interacting with multiple layers.
  802.21 Facilitates handover determination
  802.21 Provides a technology-independent unified interface to upper layers and MIH users
  802.21 facilitates both station initiated and network initiated handover determination. Both local and remote triggers are supported
Design Assumptions Don’ts
  802.21 does not modify existing handover principles
  802.21 does not mandate handover determination based on 802.21 events. Events are informational in nature

## Slide 8
Media Independent Services
Media Independent Services Dos:
  Mobility Management Entities access 802.21 services through well defined SAPs
  More than one user can have access to 802.21 services in order to integrate multiple mobility protocols (E.g., Cellular –MIP)
  802.21 services could be invoked to request operations on underlying resources
Media Independent Services Don’ts
  802.21 does not replaces existing mobility management function and protocols already in place
Notes: An 802.21 user is able to access 802.21 services through well defined service access points. Thus information commands an events are delivered through these SAPs using 802.21 services primitives. Services are available simultaneously to one or more users. An actual implementation however is likely to provide a single mobility management function availing of 802.21 services an requesting operations on underlying link layer interfaces. 802.21 itself however does not replace existing mobility management technologies and does not have any impact on the handling of intra-technology handovers.

## Slide 9
Media Independent Services (cont’d)
Media Independent Services:
  Event Service Dos
    Local and Remote Events are supported
    Events indicate changes in state behavior
    Events indicate administrative state change
    Events facilitate handover detection
    Events are delivered according to 802.21 users preferences
  Events Service Don’ts
    Events do not propagate directly between heterogeneous stacks
    Events do not enforce actions but rather suggest them
Notes: The next set of slides address the three services provided by 802.21 and what their dos and don’ts. The Event Service primarily provide information with regards to possible changes in behavior such as poor radio conditions or low throughput. Changes in administrative state (disable devices) might also trigger a 802.21 event. Note however that 802.21 events do not propagate across heterogeneous technologies. E.g., radio environment measurements are not passed from 8025o Cellular. The information provided by 802.21 event is informative in nature as does not enforce any particular procedure on receipt of these events. Rather 802.21 are suggestions that can be used by 802.21 user to decide whether a link layer interface switch should take place.

## Slide 10
Media Independent Services (cont’d)
Media Independent Services:
  Information Service Dos
    Provides heterogeneous network information within a particular geographical area
    Information might be delivered through access technology broadcast/multicast procedures or through data base queries at a remote server
    Information services might be dynamic or static
  Information Service Don’ts
    802.21 does not define how the information server is accessed, but only what information is required
    802.21 does not specify how the information service might be implemented in a particular technology
Notes: Information services can be provided either over-the-air or by accessing information servers over the internet. Information services provide information such as neighbor lists and network capabilities that can be useful for the detection and selection of an alternate network. Note that when information is not access over 802 technologies, 802.21 does not address the procedures that allow a client to access the information server but only the content of the information.

## Slide 11
Media Independent Services (cont’d)
Media Independent Services:
  Command Service Dos
    Commands might flow from the 802.21 MIH user to 802.21 MIH and from 802.21 MIH to link layer entities
    Commands might convey 802.21MIH user decision to switch from one access technology to the other.
    Commands have both remote and local scope
    Commands might optimized existing handover mechanisms
  Command Service Don’ts
    Commands do not flow directly from one access technology to other
    Commands do not replace existing mobility management protocols and procedures.
Notes: The command service allows 802.21 users to request commands on the underlying layers on their behave. One user command (what is referred to as MIH command) might generate multiple commands from the 802.21 MIH layer to the relevant link layer interfaces. Note however that commands do not replace existing mobility management protocols. Command might propagate locally or remotely, however commands do not flow from once access technology to the other.