## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-05-0336-00-0000
Title: Reference Model and Use-Cases for 802.21 Information Service
Date Submitted: August, 2005
Presented at IEEE 802.21 session #NN in City
Authors or Source(s):
Yoshihiro Ohba, Farooq Bari, Subir Das
Abstract: This document describes reference model and potential use-cases of IEEE 802.21 Information Service. The purpose of this document is to discuss, clearly identify the scope of 802.21 Information Service with regards to IETF requirements.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3: Information Service (IS) Reference Model
802.21
IS Function
UE
802.21
IS Function
Network IS Provider (NISP)
Ia
  Ia : Interface between UE and Network IS provider
  Ix: Interface between IS function and Information Database
  Ia`: Interface between two Network IS providers
IS function is an MIH sub-function; The placement of IS function in the network will
vary depending upon specific architecture and deployment requirements.
802.21
IS Function
802.21
IS Function
802.21
IS Function
Ia
Network IS Provider (NISP)
NISP
UE
  Multi hop Model
  Single hop Model
Ia`
Information
Database
Ix
Information
Database
Ix
Depending upon the network architecture and configuration, Ix Interface can be an internal or external interface.

## Slide 4: Information Service (IS) Protocol Model
802.21
IS Function
(Client)
UE
802.21
IS Function
(Server)
NISP
Ia
IS function is an MIH sub-function; The placement of IS function in the network will
vary depending upon specific architecture and deployment requirements.
802.21
IS Function
(Client)
802.21
IS Function
(Proxy)
802.21
IS Function
(Server)
Ia
NISP
NISP
UE
  Multi hop Model
  Single hop Model
Ia`
Information
Database
Ix
Information
Database
Ix
  Ia : Interface between UE and Network IS Provider
  Ix: Interface between IS function and Information Database
  Ia`: Interface between two Network IS providers

## Slide 5: Information Service Standardization Scope
802.21
IS Function
UE
802.21
IS Function
NISP
Carried over lower layer transport (L2)
Carried over higher
layer transport
(L3 and above)
IEEE 802.21
Scope
IEEE 802.21
/IETF Scope
Information
Database
Depending upon the network architecture and configuration, Ix Interface can be an internal or external interface.
Ia
Ix
Out of Scope
Ia`
  Ia : Interface between UE and Network IS Provider
  Ix: Interface between IS function and Information Database
  Ia`: Interface between two Network IS Providers
IEEE 802.21
/IETF Scope

## Slide 6: Use-Cases
Case 1: Information Service co-located with Information Database
  Client-Server model
  Client-Proxy-Server model
Case 2: Information Service with separate Information Database
  Client-Server Model
  Client-Proxy-Server Model

## Slide 7: Case 1a:Information Service Co-located with Information Database (w/o Proxy)
802.21 IS Function/
Information
Database
(Server)
802.21 IS
Function
(Client)
Network IS Provider
UE
NISP
Ia
Ia
802.21 IS Function/
Information
Database
(Server)
IEEE 802.21/
IETF Scope
  Ia : Interface between UE and Network IS Provider
  Ia`: Interface between two Network IS Providers

## Slide 8: Case 1b: Information Service Co-located with Information Database (with Proxy)
802.21 IS Function/
Information Database
(Proxy/Server)
802.21 IS
Function
(Client)
Network IS Provider
UE
NISP
Ia
802.21 IS Function/
Information
Database
(Server)
IEEE 802.21/
IETF Scope
Ia`
IEEE 802.21
/IETF Scope
  Ia : Interface between UE and Network IS Provider
  Ia`: Interface between two Network IS Providers
Server-to-server
communication
is out of scope

## Slide 9: Case 2a: Information Service with separate Information Database (w/o Proxy)
UE
Information
Database
Information
Database
Ia
Ia
Ix
Ix
802.21 IS
Function
(Client)
Network IS Provider
802.21 IS
Function
(Server)
802.21 IS
Function
(Server)
  Ia: Interface between UE and Network
  Ix : Interface between IS Function and Information Database
Out of Scope
IEEE 802.21
/IETF Scope

## Slide 10: Case 2b: Information Service with separate Information Database (with Proxy)
UE
Information
Database
Information
Database
Ia
Ix
Ix
802.21 IS
Function
(Client)
Network IS Provider
802.21 IS
Function
(Proxy/Server)
802.21 IS
Function
(Server)
Ia`
IEEE 802.21/
IETF Scope
Out of Scope
  Ia: Interface between UE and Network
  Ix : Interface between IS Function and Information Database
IEEE 802.21/
IETF Scope
Server-to-Server
Communication
is out of scope