## Slide 1
IEEE 802.21 Media Independent Handoff Overview of services and scenarios for 3GPP2
Stefano M. Faccin
802.21 Liaison officer to 3GPP2

## Slide 2: Outline
Motivation
What is IEEE 802.21and why are we here
IEEE 802.21 Dos and Don’ts
IEEE 802.21 Reference Models
Current IEEE 802.21 Draft Scope
WLAN-3GPP2 Handovers Scenarios

## Slide 3: Motivation
To be added

## Slide 4: What is 802.21?
IEEE 802.21 is being developed to facilitate smooth interaction and media independent handover between 802 technologies and other access technologies
IEEE 802.21 Membership spans over 70 members from more that 20 companies in over 10 Countries
IEEE 802.21 offers an open interface that:
  provides link state event reporting in real time (Event Service)
  provides intersystem information, automatically and on demand (Information Service)
  allows a user to control handover link state (Command Service)

## Slide 5: Why are we here?
Work actively within relevant standard bodies in order to introduce applicable IEEE 802.21 requirements (E.g., where does IEEE 802.21 fit?)
Update relevant 3GPP2 groups with latest development in IEEE 802.21 standards
Request your feed back and support in the determination of the optimal placement of IEEE 802.21 Functions
Enthuse the 3GPP2 community about the development of requirement on IEEE 802.21 technology

## Slide 6: Some Definitions
Media Independent Handover Function (MIHF):
  MIH is a cross-layer entity that provides mobility support through well defined Service Access Points offering Event, Information and Command services
MIH User:
  A local entity that avails of MIHF services through the MIH Service Access Points
MIH Network Entity:
  A remote entity that is able to communicate with an MIHF over a transport that supports Media Independent Services

## Slide 7: IEEE 802.21 DOs and DON’Ts
DOs:
  specifies procedures that facilitate handover decision making, providing link layer state information to MIH users. Enabling low latency handovers across multi-technology access networks
  defines the methods and semantics that facilitate the acquisition of heterogeneous network information and the basic content of the this information, thereby enabling network availability detection
  specifies command procedures that facilitate seamless service continuity across heterogeneous networks
DON’Ts:
  IEEE 802.21 neither executes handovers nor defines handover policies leading to handover execution
  IEEE 802.21 neither controls network detection nor specifies network selection procedures

## Slide 8: 802.21 Overview
IEEE 802.21 standard consists of:
  An architecture that enables transparent service continuity while a mobile node (MN) switches between heterogeneous link-layer technologies
  A set of handover-enabling functions within the mobility-management protocol stacks of the network elements and the creation therein of a new entity called the MIH Function (MIHF)
  The definition of Media Independent Service Access Point (MIH_SAP) and associated primitives are defined to provide MIH users with access to the services of the MIHF
  The definition of new Link Layer SAPs and associated primitives for each specific access technology

## Slide 9: 802.21 Overview (cont.d)
The MIH Function provides three services:
  Event Service detects events and delivers triggers from both local as well as remote interfaces
    E.g. Link_available, Link_up, Link_down, etc.
  Command Service provides a set of commands for the MIH users to control handover relevant link states
    E.g. MIH_Link_Switch, MIH_Configure_Link, MIH_Handover_Initiate, etc.
  Information Service provides the information model and an information repository to make more effective handover decisions. The mobile terminal obtains information from the repository using its current network points of attachment
    E.g. list of available networks, network operator, IP version, neighbor information, etc.

## Slide 10: Design Assumptions
DOs:
  Cross-layer entity interaction with multiple layers
  Facilitate handover determination through a technology-independent unified interface to MIH users
  Facilitate both station initiated and network initiated handover determination
DON’Ts:
  Does not modify existing handover principles
  Does not mandate handover determination based on IEEE 802.21 events

## Slide 11: IEEE 802.21 Model Terminal Side
Media Independent Handover Function
(
MIH
)
802
.
3
802
.
11
802
.
16
802
LINK LAYER
3
GPP2 LINK LAYER
Link Layer
Media Independent Handover User
Information
MIH
Commands
MIH
Events
Link
Events
Link
Commands
Information
…
MIH User
1
MIH User n
MIH User
2

## Slide 12: IEEE 802.21 Model Network Side
Media Independent Handover Function
802
.
3
802
.
11
802
.
16
802
Access Network
3
GPP2
Network
MIH Network Entity
Information
MIH
Commands
MIH
Events
Link
Events
Link
Commands
Information
...
802
.
11
MIH
Network
Entity
?
Higher Layer Transport
Higher Layer
/
L
2
Transport
802
.
16
MIH
Network
Entity
3
GPP2 MIH
Network
Entity

## Slide 13: Overall 802.21 Model
LLC
MAC
PHY
3
GPP2
Interface
E
v
e
n
t
s
E
v
e
n
t
s
MAC
PHY
Media Independent Handover Function
E
S
/
C
S
/
I
S
E
v
e
n
t
s
E
v
e
n
t
s
802
Interface
Client
Station
802
Network
Network
Media Independent Handover Network Entity
(
E
.
g
.
,
MIH Server Controller
)
Media Independent Handover
Function
Media
Independent
Handover User
Media
Independent
Handover User
Information Service over L
2
Transport
Higher Layer
Transport
/
L
2
Remote MIH Events
/
MIH Commands over L
2
Transport
Higher Layer
Transport
(
E
.
g
.
,
IP
)
IS
/
CS
/
ES over higher layer transport
E
S
/
C
S
/
I
S
Leyend
:
ES
/
CS
/
IS
:
Event Service
/
Command
Service
/
Information Service
?
:
Interface TBD
LLC
:
Logical Link Control
MAC
:
Medium Access Control
PHY
:
Physical Layer
MIH
:
Media Independent Handover
Higher Layer
Transport
E
S
/
C
S
/
I
S
LLC
3
GPP2

## Slide 14: Media Independent Services
DOs:
  MIH users access IEEE 802.21 services through well defined SAPs
  More than one MIH user can have access to IEEE 802.21 services in order to integrate multiple mobility protocols
  IEEE 802.21 services could be invoked to request operations on underlying resources
DON’Ts:
  IEEE 802.21 does not replaces existing mobility management function and protocols already in place

## Slide 15: Media Independent Event Service
DOs:
  Local and Remote Events are supported
  Events might indicate link layer or physical layers state changes in real time
  Events facilitate handover detection
  Events are delivered according to IEEE 802.21 users preferences
DON’Ts:
  Events do not propagate directly between heterogeneous stacks
  Events do not enforce actions but rather suggest them

## Slide 16
Media Independent Information Service
DOs:
  Provides heterogeneous network information within a particular geographical area
  Information might be delivered through access technology broadcast/multicast procedures or through data base queries at a remote server
  Information services are static in nature
DON’Ts:
  IEEE 802.21 does not define how the information server is accessed, but only what information is required
  IEEE 802.21 does not specify how the information service might be implemented in a particular technology

## Slide 17
Media Independent Command Service
DOs:
  Commands might flow from the IEEE 802.21 MIH user to IEEE 802.21 MIH and from IEEE 802.21 MIH to link layer entities
  Commands might convey IEEE 802.21MIH user decision to switch from one access technology to the other
  Commands have both remote and local scope
DON’Ts:
  Commands do not flow directly from one access technology to other
  Commands do not replace existing mobility management protocols and procedures

## Slide 18: 802.21 Design Principles
Design Assumptions DOs:
  802.21 cross-layer entity interacting with multiple layers
  802.21 Facilitates handover determination
  802.21 Provides a technology-independent unified interface to upper layers and MIH users
  802.21 facilitates both station initiated and network initiated handover determination. Both local and remote triggers are supported
Design Assumptions DON’Ts
  802.21 does not modify existing handover principles
  802.21 does not mandate handover determination based on 802.21 events. Events are informational in nature

## Slide 19: Scope of Current 802.21 Draft
Media Independent Handover Principles and Design Assumptions
Supported Media Independent Services
Service Access Points and their Primitives
A protocol for the transport of Media Independent Handover services

## Slide 20: 802.21 @ L2 vs. 802.21 @ L3
802.21 remote IS, ES and CS require a “transport”
Transport can be:
  @ L2:
    L2 specific signalling is used
    E.g. in 802.11 TGu will define transport of 802.21 IS
    For IS, applicable to both current and target access
802.11-AN
UE
IP
MIHFNW
AP
MIHFUE
MIHFNW
Out of scope of 802.21
802.21 transported in L2 frames

## Slide 21: 802.21 @ L2 vs. 802.21 @ L3 (cont.d)
  @ L3 and above:
    Use existing IP connectivity to access and MIHF in the network
    Effort to define 802.21 IS transport @ L3 and above has started in IETF
UE
3G-PDN
WiMAX
PDN
802.16-AN
802.11-AN
IP
MIHFNW
MIHFUE
UE
IP
MIHFNW
MIHFUE
UE
IP
MIHFNW
MIHFUE
802.21 transported @ L3 or above
MIHFNW
MIHFNW
MIHFNW
In scope of 802.21/IETF

## Slide 22: 802.21 @ L2 vs. 802.21 @ L3 (cont.d)
Usage of L2 versus L3 and MIH services:
3G-PDN
MIHFNW
Internet
Current active connection
802.11-AN
MIHFNW
802.21 @ L3
(IS, ES and CS)
UE
MIHFUE
802.21 @ L2
(IS => TGu)
3G-PDN
MIHFNW
Internet
Current active connection
802.11-AN
MIHFNW
802.21 @ L3
(IS, ES and CS)
UE
MIHFUE
No 802.21 @ L2
Legacy (pre-TGu WLAN)
TGu-enabled WLAN)
3G Operator
3G Operator

## Slide 23
802.21 @ L2 vs. 802.21 @ L3 (cont.d)
Usage of L2 versus L3 and MIH services:
3G-PDN
MIHFNW
Internet
Current active connection
802.11-AN
802.21 @ L3
(IS, ES and CS)
UE
MIHFUE
No 802.21 @ L2
Legacy (pre-TGu WLAN)
TGu-enabled WLAN)
802.21 @ L2
(IS => TGu)
3G-PDN
MIHFNW
Internet
Current active connection
802.11-AN
802.21 @ L3
(IS, ES and CS)
UE
MIHFUE
3G Operator
3G Operator

## Slide 24
802.21 @ L2 vs. 802.21 @ L3 (cont.d)
Usage of L2 versus L3 and MIH services MIH outside 3G-PDN:
3G-PDN
MIHFNW
Internet
Current active connection
802.11-AN
802.21 @ L3
(IS, ES and CS)
UE
MIHFUE
No 802.21 @ L2
Legacy (pre-TGu WLAN)
TGu-enabled WLAN)
802.21 @ L2
(IS => TGu)
3G-PDN
MIHFNW
Internet
Current active connection
802.11-AN
802.21 @ L3
(IS, ES and CS)
UE
MIHFUE
3G Operator
3G Operator
3G Operator
3G Operator

## Slide 25
3GPP2-WLAN Example
MME
/
MIHF
-
NW
802
.
11
AN
AS
/
NAS
3
G
-
PDN
STA
/
UE
802
.
11
802
.
21
MIH
User
Client
MIH COMMAND
LINK EVENT
MIHEVENT
LINK COMMAND
MIH REMOTE EVENT
(
link
_
info
)
MIHCOMMAND
CELL
_
DCH
1
.
2
.
4
.
5
.
6
.
7
.
17
.
18
.
19
.
20
.
21
.
MIH EVENT REGISTRATION REQUEST
MIH EVENT REGISTRATION RESPONSE
Beacon
Not Associated
Previous MIH
“registration”
3
.
8
.
Favorable Network
=
>
Selection
MIH REMOTE COMMAND REQUEST
L
3
Switch request
(
link
_
info
)
15
.
14
.
16
.
13
.
12
.
11
.
10
.
9
.
URA
_
PCH
Associate
/
Authenticate
LINK EVENT
LINK COMMAND
MIH REMOTE COMMAND RESPONSE
L
3
Mobility
(
e
.
g
.
Mobile IP
)
TO BE REDESIGNED FOR 3GPP2

## Slide 26
WLAN-3GPP2 Example
TO BE REDESIGNED FOR 3GPP2

## Slide 27: Conclusions
3GPP2 has identified inter-system/inter-technology mobility requirements that might benefit from IEEE 802.21 services
IEEE 802.21 would like to work together with 3GPP2 experts to find how IEEE 802.21 might satisfy these requirements

## Slide 28: Appendix: Background Slides

## Slide 29: Model for Event Service
ES in local entity
Remote Link Events (e.g. from terminal to MIHF in network)
Remote MIH Events (e.g. from terminal to MIHF in network)

## Slide 30: Model for Command Service
CS in local entity
Remote Commands (e.g. from MIHF in network to terminal)
Remote Commands (e.g. from MIHF in network to terminal)