## Slide 1: Higher layer services and information IEs
What we already have:
  IP subnets (per PoA)
  PoA capabilities bitmap (per PoA)
    Security Available (y/n)
    QoS Available (y/n)
    Internet Access Available (y/n)
    IP Version 4 supported (y/n)
    IP Version 6 supported (y/n)
    Emergency Services available (y/n)
    Others
Newly proposed:
  IP address configuration method supported (per PoA?)
  DHCP address (per PoA or per AN?)
  AAA address (per PoA or per AN?)
  Others?

## Slide 2: How to incorporate the new IEs (Option 1)
Option 1: Add them in parallel to the existing IEs in Table 6 under per PoA higher layer services/info. For example:
No | Name of Information Element | Description | Representation | Length (octets)
4.3 | TYPE_IE_POA_IP_CONFIG_METHODS | IP address configuration method supported | bitmap | 
4.4 | TYPE_IE_POA_ DHCP_ADDR | DHCP address | IP address | 
4.5 | TYPE_IE_POA_ AAA_ADDR | AAA address | IP address | 

## Slide 3: How to incorporate the new IEs (Option 2a)
Option 2a: Add them to the existing POA capabilities IE in Table 6 (of cause we no longer can use the bitmap representation):
No | Name of Information Element | Description | Representation | Length (octets)
4.2 | TYPE_IE_POA_ CAPABILITIES | A list of PoA capabilities | Security Available Y/N QoS Available Y/N Internet Access Available Y/N IP Version 4 supported Y/N IP Version 6 supported Y/N Emergency Services Y/N IP Address config methods bitmap DHCP address IP addr AAA address IP addr (Others) | variable

## Slide 4: How to incorporate the new IEs (Option 2b)
Option 2b: Should there be an Access Network specific capabilities IE in Table 6?
No | Name of Information Element | Description | Representation | Length (octets)
2.7 | TYPE_IE_AN_ HIGH_LAYER_ CAPABILITIES | A list of AN higher layer capabilities | IP Address config methods bitmap DHCP address IP addr AAA address IP addr | variable
4.2 | TYPE_IE_POA_ CAPABILITIES | Bitmap of PoA capabilities | Security Available Y/N QoS Available Y/N Internet Access Available Y/N IP Version 4 supported Y/N IP Version 6 supported Y/N Emergency Services Y/N (Others) |