## Slide 1
IEEE 802.21 MEDIA INDEPENDENT HANDOVER
DCN: 21-07-0xxx-00-0000
Title: Information Service & IEEE 802.16 ND&S
Date Submitted: January, 09, 2007
Presented at IEEE 802.21 teleconference
Authors or Source(s):
Ronny Kim
Abstract: This presentation shows additional 802.16 amendments.

## Slide 2
  IEEE 802.21 presentation release statements
This document has been prepared to assist the IEEE 802.21 Working Group. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
The contributor grants a free, irrevocable license to the IEEE to incorporate material contained in this contribution, and any modifications thereof, in the creation of an IEEE Standards publication; to copyright in the IEEE’s name any IEEE Standards publication even though it may include portions of this contribution; and at the IEEE’s sole discretion to permit others to reproduce in whole or in part the resulting IEEE Standards publication. The contributor also acknowledges and accepts that this contribution may be made public by IEEE 802.21.
The contributor is familiar with IEEE patent policy, as outlined in Section 6.3 of the IEEE-SA Standards Board Operations Manual <http://standards.ieee.org/guides/opman/sect6.html#6.3> and in Understanding Patent Issues During IEEE Standards Development http://standards.ieee.org/board/pat/guide.html>

## Slide 3: IEEE 802.16 ND&S
4 Steps of ND&S
  NAP Discovery
  NSP Discovery
  NSP Enumeration and Selection
  ASN Attachment based on NSP Selection
Two deployment cases
  “NAP+NSP” deployment case
    An ASN(Access Service Network) managed/owned by a single NSP administrative domain
  “NAP sharing” deployment case
    An ASN managed by a NAP but shared by two or more NSPs.
NAP Discovery
  DL-MAP of ASN
  Operator ID
    Most significant 24 bits of “Base Station ID”

## Slide 4: IEEE 802.16 ND&S (more)
NSP IDs over SII-ADV and/or SBC-RSP
  Only when NSP Identifier Flag is set
MS depends on the Configuration Information stored in the MS.
  NAP ID list, NSP ID list, NAP/NSP mapping list, NSP Change Count, Mapping table between 24-bit NSP IDs and Corresponding realm of the NSPs.
  Physical information, Security parameters, Network deployment mode.

## Slide 5: IEEE 802.16 ND&S (more)
MS depends on the Configuration Information stored on the MS.
  NAP ID list
  NSP ID list
  NAP/NSP mapping list
  NSP Change Count
  Mapping table between 24-bit NSP IDs and Corresponding realm of the NSPs.
  Physical information
  Security parameters
  Network deployment mode.

## Slide 6
Information Element | Description | Comments
General Network Information (List of Networks) |  | 
Network Type | List of all Network types that are available in a particular area | E.g., 802.11, 802.16, CDMA, UMTS Networks (Table-8)
Operator Identifier | Core Network Identifier | Operator Type + Operator name
Service Provider | Provider of services | Service Provider name
802.21 Information Elements-1

## Slide 7
Information Element | Description | Comments
Access Network specific Information |  | 
Access Network Identifier | Used to uniquely identify access network. | 
Roaming Partners | Roaming partners that have agreement with Access Network operator | 
Network Standards | Access Network specific applicable revisions to base standards | (802.16-2001, 802.16c-2002,802.15a- 2003,802.16-2004, 802.16e-2005, 802.16g-2007
Cost | Cost of accessing the network | Currency+Unit+Value+Service-Info (Table-10)
Security | Authentication Methods and Cipher Suites | 
QoS | Packet Transfer Delay (Min/Max/Avg) Jitter Packet Loss Rate Packet Error Rate | 
802.21 Information Elements-2

## Slide 8
Information Element | Description | Comments
PoA specific Information |  | 
Address | MAC Address | 
Location | PoA location | See Table 11,12,13
Data Rate | Min-Max Range | 
Channel Range | Spectrum Range | 
Subnet Information | List of subnets to which PoA belongs | 
PoA Capabilities | Services Supported | 
IP Config Methods | DHCP, etc. | 
802.21 Information Elements-3

## Slide 9: 802.16 ND&S Call Flow

## Slide 10
Information Service – Multicast

## Slide 11
Information Service – Unicast

## Slide 12: Summary
The amendment is for Media Independent Network Discovery.
  Same mechanism as IEEE 802.11
Stored information in the MS is very static.
Information expected to be stored in the MS can be obtained through information service.
802.21 IS can complement 802.16 ND&S
Limitation of the length of query and query response can be discussed.