## Slide 1
Power Budget Proposals adhoc Report
IEEE 10GE-PON
2. March, 2007

## Slide 2
Supporters
Hitachi, KDDI, Mitsubishi, NEC, NTT, OKI, Sumitomo, Fujitsu
Hiroki Ikeda, hiroki.ikeda.qp@hitachi.com
Keiji Tanaka, kj-tanaka@kddilabs.jp
Junichi Nakagawa, Nakagawa.Junichi@ay.MitsubishiElectric.co.jp
Satoshi Shirai, Shirai.Satoshi@db.MitsubishiElectric.co.jp
Naoto Saeki, n-saeki@bl.jp.nec.com
Tomoaki Masuda, t-masuta@bq.jp.nec.com
Hiroki Yanagisawa, yanagisawa@ay.jp.nec.com
Seigo Takahashi, sei5@ax.jp.nec.com
Akihiro Ootaka, ootaka@ansl.ntt.co.jp
Tsutomu Tatsuta, tatsuta@ansl.ntt.co.jp
Kenichi Suzuki, kenyichi@ansl.ntt.co.jp
Toshiaki Mukoujima, mukoujima380@oki.com
Shinji Tsuji, stsuji@sei.co.jp
Tetsuya Yokomoto, tyoko@access.fujitsu.com
Hiroshi Hamano, hamano.hiroshi@jp.fujitsu.com
Motoyuki Takizawa, mtaki@access.fujitsu.com

## Slide 3
Suggests 10GE-PON optical PHY structures, which
co-exists with 1G system and
achieves ClassB++, 29dB channel insertion loss.
Channel insertion loss (CH IL) :
PX10(20dB), PX20(24dB), ClassB++(29dB)
Optical wavelength (under study) :
1G U/S : 1.31um D/S : 1.49um
10G U/S : 1.31um (TDMA overlay), 1.59um (WDM overlay)
D/S : 1.57um
Figures in the discussion are assumed to be product specs.,
considering the worst case,
not the world top data, nor those under the typical condition.
Under ITU-T specs., 10G optical transceiver figures are discussed,
which includes all the component-oriented penalties
and excludes only Path Penalty.
Additional penalties for OLTs and/or ONUs are not yet discussed,
e.g. WDM filter insertion loss, Burst mode penalty, and ONU wide temp. range.
Power Budget Considerations

## Slide 4
Optical Component Assumptions
 |  | Conditions | Vender suggestion range |  | 
 |  |  | worst | best | Prospects
Receiver Sensitivity [dBm] | PIN | ER>8.2 (EML) | -16 | -17 | 
 | APD | ER>8.2 (EML) | -24 | -25 | 
 |  | ER >6 (DFB) | -20 | -23 | 
Transmitter Output Power [dBm] | DFB | Uncooled | -1 | -0.5 | 
 |  | Cooled | +3 | +4 | +5.5
 | EML |  | 0 |  | +3
 | SOA |  | +6 | +8 | +12?
FEC Improvement [dB] | RS | PIN Receiver | 3 |  | 
 |  | APD Receiver | 3 | 4.5 | 
 | E-FEC |  | 4 | 5.5 | 

## Slide 5
Cost Assumptions
 | Lee | Gokhale | A | B | C | D
PIN ROSA | 1 | 1 | 1 | 1 | 1 | 1
APD ROSA | 3 | 3 | 7 | 10 | 3.5 | 3
DML TOSA | 2 |  | 2 | 2.5 – 8 | 2 | 2 (Single Lens) 4 (Double Lens) 6 (TEC)
EML TOSA | 10 | 10 | 8 | 10 | 6 | 10
SOA | 20 | 20 | 30 | 30 | 20 | 20
EDFA | 40 | 50 | 50 | 40 | 50 | 50
EML+SOA (int.) |  | 20 | 35 |  | 25 | 
DFB+SOA+EA (C-band) |  | 15 |  |  |  | 
Assumptions are based on the component cost available today.
APD ROSA cost differs among venders.

## Slide 6
10G : 1571nm
10G : 1571nm
Two options : 1G/10G WDM ovrelay or TDMA overlay
- Optical preamplifier in 10G OLT is required to achieve ClassB++
using 10G optical transceiver products available today --- WDM overlay
- Output power and performance improvements of optical signal source
lead to a more cost-effective transceiver configuration --- TDMA overlay
WDM overlay
- Optical preamplifier with narrow-band
noise-rejection filter in 10G OLT
- 1G/10G independent structure
- More  needed for 10G U/S
TDMA overlay
- Optical preamplifier not feasible because
of 1G-signal rejection by NB filter
- 3 dB output power increase required
for signal sources to achieve ClassB++
Upstream
1G/10G-OLT
1G-ONU
1G-ONU
10G-ONU
1G/10G : 1311nm
1G : 1491nm
Dual-rate PMD
1G-OLT
10G-OLT
1G-ONU
1G-ONU
10G-ONU
1G : 1311nm
10G : 1591nm
1G : 1491nm
Optical Preamp with NB Filter

## Slide 7
Power Budget Proposals (U/S) --- TDMA Overlay
# | RX --- TX Pair | PB (*1) | PP(*2) | Tx | Rx | FEC RS | Cost 1:32 | Data Range | 
1 | APD----------DFB | 23 / 22+1 27 / 25+2 | 2 1 | -1 -0.5 | -20 -23 | 3 4.5 | 1 | worst best | Uncooled DFB
 |  | 30 / 29+1 |  | +4- 5.5 |  |  | 1.2- 2.9 | Pros-pect | Cooled DFB
2 | APD----------EML | 27.5 / 25.5+2 28 / 27+1 | 2 1 | 0 | -24 | 3 4 | 4.8 2.9 | worst best | 
 |  | 30 / 29+1 |  | +2 |  |  |  | Pros-pect | High power EML
Power Budget Proposals (U/S) --- WDM Overlay
# | RX --- TX Pair | PB (*1) | PP(*2) | Tx | Rx | FEC RS | Cost 1:32 | 
1 | PD/Pre------EML | >31 / 29+2 | 2 | 0 | <-27 | 3- 4.5 | 4- 5 | 
(*1)PB: Power Budget (/CH IL＋PP), (*2) PP: Path Penalty
1G/10G : 1.31um
1G : 1.31um, 10G : 1.59um
EML can be replaced by other signal sources, such as, MZ modulator with CW-LD.
(*1)PB: Power Budget (/CH IL＋PP), (*2) PP: Path Penalty
EML can be replaced by other signal sources, such as, MZ modulator with CW-LD.
Note: Each column shows its own data range individually.
Sum of the figures along lines is NOT indicating ‘Power Budget’.

## Slide 8
Downstream
Two options : PIN or APD@ONU
- Optical power level shifts drastically depending on the PD choice
- Vender opinions are divided for ClassB++; PIN:APD = 3:3
PIN@ONU
- Cost minimum
- Optical amplifier for all the classes
- High-power SOA reliability issue
+12dBm@ClassB++ may be necessary
EDFA another choice
- Fiber non-linearity issue
- Single ONU for all the classes
APD@ONU
- Depends on APD cost reduction scope
- High-power EML may eliminate SOAs
- Single APD-ONU or mixed for classes
PIN for PX10,20 and APD for ClassB++
EML
SOA
APD-ONU
+3dBm
-24dBm
EML
SOA or
EDFA
PIN-ONU
+12dBm
-16dBm

## Slide 9
Power Budget Proposals (D/S) --- PIN@ONU
# | TX --- RX pair | PB (*1) | PP(*2) | Tx | Rx | FEC RS | Cost 1:32 | Data Range | 
1 | EML/SOA-----PIN | 25 / 23+2 28 / 26+2 | 2 | +6 +8 | -16 -17 | 3 | 2 1.5 | worst best | 
 |  | 31 / 29+2 |  | +12? |  |  |  | Pros-pect | High Power SOA
2 | EML/EDFA----PIN | >31 / 29+2 | 2 | +11 +12 | -16 -17 | 3 | 2.3 2 | worst best | only for ClassB++
(*1)PB: Power Budget (/CH IL＋PP), (*2) PP: Path Penalty
Power Budget Proposals (D/S) --- APD@ONU
# | TX --- RX pair | PB (*1) | PP(*2) | Tx | Rx | FEC RS | Cost 1:32 | Data Range | 
3 | EML-----------APD | 26 / 24+2 29 / 27+2 | 2 | -1.5 0 | -24 -25 | 3.5 4 | 8 2.5 | worst best | 
 |  | 31 / 29 +2 |  | +3 |  |  |  | Pros-pect | High Power EML
4 | EML/SOA----APD | >31 / 29+2 | 2 | >+3 >+5 | -24 -25 | 3 4 | 9 3 | worst best | only for ClassB++
EML can be replaced by other signal sources, such as, MZ modulator with CW-LD.
(*1)PB: Power Budget (/CH IL＋PP), (*2) PP: Path Penalty
1G : 1.49um, 10G : 1.57um
1G : 1.49um, 10G : 1.57um
EML can be replaced by other signal sources, such as, MZ modulator with CW-LD.
Note: Each column shows its own data range individually.
Sum of the figures along lines is NOT indicating ‘Power Budget’.

## Slide 10
Mitsubishi Proposal
takahashi_1_0706.pdf, IEEE 802.3av SG, SanDiego, July 2006

## Slide 11
Experimental Configuration
 | Transmitter | Receiver | Remarks
D/S config. | EA-DFB | APD | 20km SMF, λ=1539nm, 10.3Gbps, NRZ PRBS 231-1
Error rate measurement
  Output power:
  +5.6dBm
  Receiver sensitivity
  after 20km SMF:
  -26.7dBm@BER10-10 (※)
  Loss budget:
  32.3dB (※)
  ※ measured w/o FEC
after 20km SMF
Sample devices – EA-DFB: Opnext LE7062VSTS, APD: Opnext PS7055STS
97 ps
Sample data of 10Gbps downstream
Hitachi Proposal

## Slide 12
Issues
FEC
- RS（255/239） Mandatory
Sensitivity improvements depend on the optical components;
RX : PIN, APD, or Optical preamp. (Noise source).
TX : Direct-modulated DFB or EML (ER, ISI).
Assumptions differ among venders.
- In-band FEC Mandatory
Rate-increase penalty may be fatal to ClassB++
- More Discussion needed for Enhanced-FEC
Tradeoffs between the increments and burst-mode CDR risks
EDC
- U/S TDMA / D/S WDM overlay : no EDC necessary
- U/S, D/S WDM overlay : Some component options may need it

## Slide 13
Developments for optical signal sources
- Higher power to achieve ClassB++
- Improvement of ER, relaxation oscillation freq., and eye opening
- ONU wide operational temperature range
- 10G high-current laser driver
Reduction of additional penalties is a must, esp. PON relations
- WDM filter insertion loss and crosstalk
- Burst-mode penalty
- Dual-mode PMD;
10G best performance necessary
1G/10G power level difference; overload, LOP (Loss of Power)
Discussions on ITU-T specs.
- Practical figures availability in productions and experiments
- Translation to IEEE specs. required for IEEE Drafts
Issues (continued)

## Slide 14
Summary
Upstream :
TDMA overlay is supposed to be a suitable target for a practical ClassB++
transceiver configuration, expecting new higher-power optical signal sources,
compared to WDM overlay with optical preamp. in OLT.
Downstream :
PIN@ONU seems so far the minimum cost approach,
but several venders prefer APD and further discussions are needed.
Further Investigation :
- Developments for higher power optical signal sources
- Reduction of additional penalties, especially PON relations
- ITU-T specs. translation into IEEE Drafts
Next Step :
- Tentative figures for 10GE-PON PHY spec. sheets
- Discussions among venders;
DFB or EML, Power targets for signal sources,
PIN or APD, Assumptions for a variety of penalties