## Slide 1: TP3 (Informative) Simple Rx Sensitivity Test
Sudeep Bhoja Big Bear Networks

## Slide 2: Background
Table 68.4 has TBD for Bessel-Thompson Filter Bandwidth
  Informative test of Fig 68-9
Previously popescu_1_0904 suggested BT4 of 2.3GHz
  300m of Cambridge 65 fiber model
  However, connector effects were not included
  No final conclusion was reached
Simulated Fiber Model details
  300m of Cambridge 108 fiber model
  2 worst case connectors at 7um offsets
  47.1ps (20-80%) rise time, 7.5GHz BT4 Rx filter
  6.5dB of dispersion budget
Symmetric impulse responses were automatically sorted from model
  PIE-D range was 4.5 +/- 0.5dB
  DC group delay of the pulse response was computed
    Measure of “center of gravity” of pulse
  This is then compared to the location of main peak
  Pulse is declared symmetric if DC Group Delay is within 3% of main peak location

## Slide 3: Fit to Fiber Model
2GHz has good average fit to Quasi-symmetrical pulses
  Results in PIE-D of ~4.75dB.
Good agreement between PIE-D and finite EDC
Recommend 2GHz BT4 as the filter.
2GHz BT4 filter