## Slide 1: STS-1 synchronous payload envelope
STS-1 Envelope Capacity
9 rows
90 bytes
3 bytes
87 bytes
1
2
3
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
87
Transport
Overhead
STS
Pointer
STS-1
Synchronous
Payload
Envelope
62

## Slide 2: STS-1 payload pointer offset
STS Pointer
Frame N
STS Pointer
Frame N + 1
STS-1 SPE
125 µs
250 µs
1
40
41
87
90 bytes
63
Notes: The pointer overhead bytes carry a binary number that is an offset, in bytes, into the envelope capacity to the beginning of the next SPE frame.

## Slide 3: Why pointers exist - SPE phase identification
DS3
DS3
DS3
Path
Termination
Path
Termination
Path
Termination
OC-1
OC-3
STS-1 SPE
125 us
SONET Hub
(Line Terminating Equipment)
OC-1
OC-1
67
Notes: The pointer mechanism serves two key purposes; the first is SPE phase identification, and the second is SPE frequency justification. The need for SPE phase identification is illustrated in the above slide.
Consider a SONET hub that is multiplexing the SPEs from three separate OC-1s into a single OC-3. Although we could assume that the arriving SPEs are aligned within the corresponding STS-1 SPE capacities, we cannot assume that the arriving STS-1 frames are aligned since they have arrived from different places.
SONET requires that the STS-1s within an STS-N be frame aligned so that the transport overhead from each STS-1 can be combined and used as the transport overhead for the STS-N. One way to align the incoming STS-1s would be to use a 125usec buffer to delay the early arrivals to align with the latest arrival. However, 125usec delay in every transport network element results in an unacceptably high additional propagation delay for delay sensitive services such as voice. Furthermore, if any of the incoming OC-1s is not perfectly synchronous with respect to the hub, then the buffer will periodically overflow or underflow, causing corruption of the payload.
The SONET solution is to decouple the phase alignment of the SPE from that of the STS-1 and use a pointer to indicate the offset. Thus buffers are not required and the SPE encounters minimal delay through the hub.

## Slide 4: Why pointers exist - SPE frequency justification
f1
Example: f2 > f1 > f3
DS3
DS3
DS3
Path
Termination
Path
Termination
Path
Termination
OC-1
OC-3
STS-1 SPE
125 us
SONET Hub
(Line Terminating Equipment)
OC-1
OC-1
f2
f3
69
Notes: The impact of imperfect network synchronization on SONET facilities is illustrated in the above slide. The hub and the first OC-1 are synchronized to the same reference, f1, whereas the second and third OC-1s are each locked to different references.
The result is that the incoming OC-1 frames, although containing exactly the same number of bytes, have different lengths when measured in time. The SPEs from these STS-1s must be transferred to STS-1s that are frame-aligned and exactly synchronous; a requirement for synchronous multiplexing. As the slide illustrates, the phase relationship between the STS-1 and the SPEs from the second and third OC-1s will be constantly changing because of the difference in frame rates.
The rate of change in this phase relationship is highly exaggerated in the example. Typically, even under worst case conditions, the offset will remain constant for some time and then change by one byte in one direction or the other. This event is called an increment operation or a decrement operation, depending on whether the pointer offset increases or decreases.

## Slide 5: STS payload pointer (H1, H2)
I - Increment Bits
D - Decrement Bits
NDF Not Set = 0110
NDF Set = 1001
Concatenation Flag
H1
H2
0
1
1
0
X
X
I
D
I
D
I
D
I
D
I
D
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Not
Used
1
0
0
1
0
0
1
1
1
1
1
1
1
1
1
1
New Data Flag
Pointer Offset
70
Notes: The contents of the STS payload pointer bytes is shown above.
Bits 7 and 8 of H1 together with bits 1-8 of H2 carry the pointer offset. If the first byte of the next SPE frame was the byte immediately following the H3 byte, the offset would contain the value 00 hex.
The bits of the pointer offset are grouped into I bits and D bits. These bits are used to flag increment operations and decrement operations respectively. A pointer processor monitoring an incoming pointer keeps track of the current offset and continuously compares the next received value with the current value. An increment operation is detected when the I bits of the received value are inverted with respect to the current value. Similarly, a decrement operation is detected when the D bits of the received value are inverted with respect to the current value.
Bits 1-4 of H1 contain the new data flag. This flag is used to notify downstream pointer processors of a change in the pointer value to a new value unrelated to the previous value. This would be used at a cross-connect system for example, when an outgoing STS-1 that was carrying an SPE from one particular incoming STS-1 suddenly starts carrying an SPE from a different incoming STS-1 due to a provisioning command. Since there is no phase relationship between the two SPEs, the pointer value will change. The new data flag is set to 1001 in the first STS-1 frame that contains the new pointer offset value, and then returns to its normal value of 0110.
When an STS-1 is concatenated to another STS-1, its pointer offset contains the value 1001001111111111. This is the concatenation flag and it effectively disables the pointer processing circuitry for this STS-1.
When a failure is detected at the path layer, path AIS is generated downstream to provide a keep-alive signal. Path AIS is detected by all ones in the H1-2 pointer bytes.

## Slide 6: STS-1 pointer processor
Pointer
Interpreter
Pointer
Generator
STS-1
STS-1 Freq.
STS-1 Frame
J1
Write
Address
Inc/Dec
Read
Address
J1
New STS-1
New STS-1 Freq.
New STS-1 Frame
New Ptr
STS-1 SPE
J1 Marker
Elastic Store (FIFO)
Comp.
Ptr
71
Notes: The STS-1 pointer processor shown above is a critical circuit that exists for every STS-1 at every line termination. This is the circuit that extracts the SPE from the incoming STS-1 after the line and section overhead have been terminated and inserts it into a new STS-1 to be transmitted onto the next line system. The frequency and phase alignment of the incoming STS-1 are derived from the received signal, whereas the frequency and phase alignment of the outgoing STS-1 is dictated by the local NE clock that is locked to the local BITS (Building Integrated Timing Supply).
The main components of the circuit are the elastic store, the pointer interpreter, and the pointer generator. The elastic store is an FIFO buffer that stores the SPE bytes as they are transferred from the incoming to outgoing STS-1. It temporarily absorbs any change in the frame phase alignment between the SPE and the outgoing STS-1.
The pointer interpreter monitors the incoming pointer to locate the SPE bytes within the STS-1 and write them into the store. The pointer generator reads the SPE bytes out of the store and inserts them into the new STS-1 along with the new pointer.

## Slide 7: Pointer increment operation
72
INC
Pointer = P
Pointer = P
Pointer = P with
Inc bits inverted
Pointer = P+1
Stuff Byte
Frame N
Frame N+1
Frame N+2
Frame N+3
H1/H2 H3
Notes: The sequence of frames shown above illustrates the increment operation.
For the frames prior to frame N, the pointer offset has had the value P. Sometime after the pointer in frame N+1 was transmitted, the pointer generator detected that the SPE frame has retreated with respect to the STS-1 frame by one byte. This offset does not show up in the frames prior to N+2 because it is absorbed by the elastic store such that the fill of the store has decreased by one byte.
In frame N+2, the pointer generator transmits the pointer value P with the I bits inverted to flag an increment operation. At the byte location immediately following the H3 byte, no byte is read out of the elastic store. A stuff byte (no information) is inserted instead.
The result is that the beginning of the next and subsequent SPE frames will be one byte later. Subsequent pointer offsets contain the value P+1 to indicate the new phase relationship.
Note that the SPE frame that crosses over between STS-1 frame N+1 and N+2 still has exactly 9 x 87 = 783 bytes in it. It is just that the space available for the SPE in frame N+2 was reduced by one byte such that it takes one byte more worth of time for those 783 bytes to be transmitted.

## Slide 8: Pointer decrement operation
73
DEC
Pointer = P
Pointer = P
Pointer = P with
Dec bits inverted
Pointer = P-1
Frame N
Frame N+1
Frame N+2
Frame N+3
H1/H2 H3
Notes: The sequence of frames shown above illustrates the decrement operation.
For the frames prior to frame N, the pointer offset has had the value P. Sometime after the pointer in frame N+1 was transmitted, the pointer generator detected that the SPE frame has advanced with respect to the STS-1 frame by one byte. This offset does not show up in the frames prior to N+2 because it is absorbed by the elastic store such that the fill of the store has increased by one byte.
In frame N+2, the pointer generator transmits the pointer value P with the D bits inverted to flag an decrement operation. The next SPE byte is read out of the elastic store into the H3 location where normally a read does not occur.
The result is that the beginning of the next and subsequent SPE frames will be one byte earlier. Subsequent pointer offsets contain the value P-1 to indicate the new phase relationship.
Note that the SPE frame that crosses over between STS-1 frame N+1 and N+2 still has exactly 9 x 87 = 783 bytes in it. It is just that the space available for the SPE in frame N+2 was increased by one byte such that it takes one byte less worth of time for those 783 bytes to be transmitted.

## Slide 9: New data operation
74
Pointer = P1
Pointer = P2 with
New Data Flag
Pointer = P2
Pointer = P2
Frame N
Frame N+1
Frame N+2
Frame N+3
H1/H2 H3
Notes: The sequence of frames above illustrates the new data operation.
The pointer offset in the frames prior to frame N has the value P1. Sometime after the pointer in frame N is transmitted, it is decided to switch a new SPE into the STS-1. The pointer in frame N+1 is transmitted with the new offset P2 and the new data flag set to 1001. The new pointer value takes effect at the offset P2.