## Slide 1: 802.3an comment resolution
Olindo Savi
Siemon
Jan 2006

## Slide 2: Background
The present 802.3an objectives call out for supporting media reach over class E (UTP or FTP) or Class F cabling (S/FTP) The present MDI spec not consistent with all cabling media types Correct approach would be to reference the present (and future) ISO/IEC 11801 standard, while maintaining interoperability to previous 60603-7 series. The present ISO/IEC 11801 standard provides a table (table 29) that summarizes the “Electrical characteristics of telecommunications outlets intended for use with balanced cabling” Table 29 provides further reference to the applicable IEC test/component standard for the MDI outlet type

## Slide 3: Current 802.3an Draft Text Draft 3.0
Calls out for IEC 60603-7 (1996)
IEC 60603-7 standard specifies unshielded RJ45 up to 3 MHz

## Slide 4: ISO-IEC 11801 Ed2.0 (2002)
Table 29 identifies current IEC 60603-7-X standard

## Slide 5
The fixed and the free connector shall be capable of interconnecting with any IEC 60603-7 series connector, and that when it is interconnected, it shall fully meet all requirements of the lower frequency 60603-7 series standard.

## Slide 6: Concluding Remarks
1. The cabling objectives call out for supporting media defined in
ISO/IEC 11801:2002. Why not follow same logic for MDI outlet?
2. Table 29 of ISO/IEC 11801:2002 provides further reference to
applicable IEC test/component standard for the MDI outlet type
3. All IEC references provided in Table 29 ensure interoperability
and backwards compatibility to previous 60603-7 series
4. Present transmission requirements in Clause 55.8 will not change

## Slide 7: Proposed Resolution
Replace the following sentence
(reference: Pg 155, sub clause 55.8.1, Line 9):
Eight-pin connectors meeting the requirements of subclause 3
and Figures 1 through 4 of IEC 60603-7: 1996
With:
Eight-pin connectors meeting the requirements of Table 29 of
ISO/IEC 11801:2002 (or later version).