## Slide 1: Low Power UTP Mode for 802.3an
Comment Text File #1

## Slide 2: Clause 28 changes to support 10GBASE-T low power UTP
Section Annex 28B.3
  Modification to priority resolution table page 25 line 56:
  Change the list in 28B.3 by placing “10GBASE-T low power UTP” as bullet (b) and renumbering other bullets.
Section Annex 28D.6
  Change bullet (h) on page 30 line 2 by inserting “and 10GBASE-T low power UTP” after “10GBASE-T full-duplex”

## Slide 3: Clause 45 changes to support 10GBASE-T low power UTP
Section 45.2.7.10
  Modify Table 45-124 as follows:
    Insert a new row and make the changes in Table 45-124, page 63 line 32 as indicated:
Bit(s) | Name | Description | R/W
7.32.11 | 10GBASE-T low power UTP | 1= Advertise PHY as 10GBASE-T low power UTP capable 0=Do not advertise PHY as 10GBASE-T low power UTP capable | R/W
7.32.10:3 | Reserved | Ignore on read | RO

## Slide 4: Clause 45 changes to support 10GBASE-T low power UTP (cont.)
Section 45.2.7.10
  Insert descriptions for the new bit and renumber the paragraphs as follows:
  Insert new description for bit 7.32.11 page 64 line 21.
    45.2.7.10.5 10GBASE-T low power UTP capability
      Bit 7.32.11 is to be used to select whether or not Auto-Negotiation will advertise the ability to operate in 10GBASE-T low power UTP PHY capability. If bit 7.32.11 is set to one the PHY will advertise 10GBASE-T low power UTP capability. If bit 7.32.11 is set to zero the PHY will not advertise 10GBASE-T low power UTP PHY capability. 10GBASE-T low power UTP capability is defined in section 55.6.3. Only full duplex operation is supported in this mode.
  Renumber remaining subsections page 64 line 28.

## Slide 5: Clause 45 changes to support 10GBASE-T low power UTP (cont.)
Section 45.2.7.11
  Modify Table 45-125 on page 65 near line 10 as follows:
    Insert new bit 7.33.10 and renumber subsequent bits accordingly
Bit(s) | Name | Description | R/W
7.33.10 | Link partner 10GBASE-T low power UTP | 1= Link partner is able to operate as 10GBASE-T low power UTP 0= Link partner is not able to operate as 10GBASE-T low power UTP | R/O
7.33.9 | Loop timing ability | 1 = Link partner is capable of Loop timing 0 = Link partner is not capable of Loop timing | R/O
7.33.8 | LP PMA training reset request | 1 = Link partner requests that Local Device reset PMA training PRBS every frame 0 = Link partner requests that Local Device run PMA training PRBS continuously | R/O
7.33.7:0 | Reserved | Value always 0, writes ignored | R/O

## Slide 6: Clause 45 changes to support 10GBASE-T low power UTP (cont.)
Section 45.2.7.11
  Insert new descriptions for bit 7.33.10 on page 66, line 7 as follows:
    45.2.7.11.6 Link partner 10GBASE-T low power UTP (7.33.10)
      This bit will only be valid when page receive bit 7.1.6 in is set to one. When read as a one, bit 7.33.10 indicates that the Link Partner is able to operate as 10GBASE-T low power UTP. When read as a zero, bit 7.33.10 indicates that the Link Partner is not able to operate as 10GBASE-T low power UTP.

## Slide 7: Clause 45 changes to support 10GBASE-T low power UTP (cont.)
Section 45.2.7.11
  Renumber subsection 45.2.7.11.6 to 45.2.7.11.7 page 66 line 7 and change text as follows:
    45.2.7.11.7 Link partner loop timing ability (7.33.9)
      When read as a one, bit 7.33.9 indicates that the Link Partner has the ability to support loop timing as specified in 55.1.3. When read as a zero, bit 7.33.9 indicates that the Link Partner lacks the ability to support loop timing.
  Renumber subsection 45.2.7.11.7 to 45.2.7.11.8 page 66 line 14 and change text as follows:
    45.2.7.11.8 Link partner PMA training reset request (7.33.8)
      If bit 7.33.8 is set to one then the Link Partner is expecting the Local Device to reset the PMA training PRBS for every PMA training frame. If bit 7.33.8 is zero then the Link Partner expects Local Device to run PMA Training PRBS continuously through every PMA Training frame.

## Slide 8: Clause 55 changes to support 10GBASE-T low power UTP
Section 55.6.1
  Insert text page 134 line 24 as follows:
    d) To negotiate that the PHY is or is not capable of supporting 10GBASE-T or 10GBASE-T low power UTP.
Section 55.6.1.2
  Modify Table 55-10
    Change page 135 line 36 U31:U21 to U31:U22
    Insert new row page 135 line 36 U21 as shown
Bit(s) | Name | Description
U31:U22 | Reserved, transmit as 0 | 
U21 | 10GBASE-T low power UTP ability (1 = support of 10GBASE-T low power UTP and 0 = no support) | Defined in 45.2.7.10.5

## Slide 9: Clause 55 changes to support 10GBASE-T low power UTP (cont.)
Section 55.6.3
  Insert new section 55.6.3 page 138 line 44
    55.6.3 Operating modes for 10GBASE-T
    10GBASE-T includes provision for multiple modes of operation. 10GBASE-T mode will support all link segments shown in Table 55-12 and defined in 55.7.2. 10GBASE-T low power UTP mode will support up to 30 meters of Class EA /Augmented Category 6 or up to 30 meters of Class F cabling.
Section 55.7
  Help needed to scale channel models accordingly

## Slide 10: Clause 55 changes to support 10GBASE-T low power UTP (cont.)
Section 55.4.3.1
  Insert text on page 119, line 1 preceding the sentence, “The values of programmable THP coefficient …” as follows:
    In 10GBASE-T low power UTP mode, the last 10 THP coefficients, ck for k=7,8,…,16, are always zero.