## Slide 1: Low Power Latency Reduction
Presentation #3

## Slide 2: Changes to support reduced latency in low power modes
Section 44.3
  Page 40, line 6 add comment to Table 44-2 column Maximum (bit time) as follows:
    Comment footnote #1) 1 Maximum bit time delay is reduced to 15,000 BT for 10GBASE-T low power UTP or 10GBASE-T low power STP.

## Slide 3: Revise section 55.6.3
Insert new section 55.6.3 page 138 line 44
  55.6.3 Operating modes for 10GBASE-T
    10GBASE-T includes provision for multiple modes of operation. 10GBASE-T mode will support all link segments shown in Table 55-12 and defined in 55.7.2. 10GBASE-T low power UTP mode will support up to 30 meters of Class EA /Augmented Category 6 or up to 30 meters of Class F cabling. 10GBASE-T low power STP will support up to 30 meters of Class F cabling. In addition to reduced reach on specified channels, 10GBASE-T low power UTP and 10GBASE-T low power STP both have reduced delay requirements as stated in 44.3 and 55.11.

## Slide 4: Revise section 55.11
Section 55.11
  Insert text immediately following the first sentence of the paragraph page 160 line 7 (section 55.11):
    For an implementation of a 10GBASE-T PHY operating in 10GBASE-T low power UTP or 10GBASE-T low power STP mode the sum of the transmit and receive data delay shall not exceed 15,000 BT.