## Slide 1
S-Parameter Measurements for the
IEEE Backplane Ethernet Task Force
David Brunker david.brunker@molex.com
Gourgen Oganessyan goganessyan@molex.com
David McCallum david.mccallum@molex.com
Molex
Lisle, Illinois
October 15, 2004

## Slide 2
GbXTM Reference Backplane
Layout and Design Overview To
Support S-Parameter Information
Backplane Dimensions:
38” x 13”
0.225”

## Slide 3
S-Parameters results presented for a 1.0 meter channel length (backplane plus daughter card)
Routing densities are consistent with GbXTM connector column pitch.
2.5 inches of total channel length is contained in each daughter card.
Routing conventions include significant stub lengths to exercise full range of channel performance.
Channels are routed through passive pinfields with non-terminated backplane connector pins.
Layout and Design Overview

## Slide 4
Construction Notes:
Relative dielectric
constant is per ParkNelco
design guide and measured
at 2.5 GHz.
Top half of board
construction is shown. Bottom
half is mirrored below central
core.
Metal layer count is 20.
Soldermask thickness
is included in total overall
thickness of 225 mils.
Board Construction

## Slide 5
Construction Notes:
Channels are edge-coupled.
Top and bottom region channels are shown.
Comparable channel construction is used in passive daughter card build.
1.0 meter channel length is represented in s-parameter data.
Channel Pitch Progression = 1.85 mm TYP
1.25 mil Copper
8.6 mil TYP
Prepreg
Height
10.5 mil TYP
Core
Height
0.6 mil Copper
Signal Height
7.75 mil TYP Trace
6.25 mil TYP Space
Board Construction

## Slide 6
Transmit–to-Receive Pin Map
Outbound/Inbound
Construction Notes:
All transmit ports initiate with J/K terminal pairs.
All receive ports terminate with G/H pairs.
Consistent transmit-to-receive pin mapping allows for only one line card port design.
8” backplane channel routing is shown.
Channels are blocked in groups of 4 transmit pairs and 4 receive pairs.
Transmit–to-Receive Pin Map
Outbound Traffic Moves Left-to-Right Tx Rx
Inbound Traffic Moves Right-to-Left Rx Tx
Pin Map

## Slide 7
Outbound Traffic – 1 meter Channel
Inbound Traffic – 1 meter Channel
Construction Notes:
Outbound
Channel routed in top of PCB.
1-meter outbound channel
vias have significant stub to assess channel robustness.
Construction Notes:
Inbound
Channel routed in bottom of PCB.
1-meter inbound channel length designed without stub to allow for channel performance comparison.
Channel Structure

## Slide 8
Channel Summary
Backplane
  Length: X1 cm (X2 inches)
  Material: Nelco N4000-13SI
Daughtercard
  Length: Y1 cm (Y2 inches)
  Material: ZZZZ
Total Length: W1 cm (W2 inches)
Stubs:
Connectors: 2 GbX

## Slide 9
S-Parameter Procedure and Mapping
Rx1
Rx2
Rx3
Rx4
Tx5
Tx6
Tx7
Tx8
Tx1
Tx2
Tx3
Tx4
Rx5
Rx6
Rx7
Rx8
Outbound
Traffic
Inbound
Traffic
Prime
Transmit
Prime
Receive
Remote
Transmit
Remote
Receive
Power Forward
Power Forward
Port 1
Port 3
Port 2
Port 4
Stimulus
Port 1 Connection Options/
Port 3 Connection Options:
J2 – J5 For Prime Transmit Tx1N – Tx4N/
K2 – K5 For Prime Transmit Tx1P – Tx4P
Insertion Loss And Far End Crosstalk
Port 2 Connection Options/
Port 4 Connection Options:
G2 – G5 For Remote Receive Rx1N – Rx4N
H2 – H5 For Remote Receive Rx1P – Rx4P
FEXT Measurements Made On Quiet Receive Line Pairs
Near End Crosstalk
Port 2 Connection Options/
Port 4 Connection Options:
G2 – G5 For Prime Receive Rx5N – Rx8N
H2 – H5 For Prime Receive Rx5P – Rx8P
NEXT Measurements Made On Quiet Receive Line Pairs

## Slide 10
Rx1
Rx2
Rx3
Rx4
Tx5
Tx6
Tx7
Tx8
Tx1
Tx2
Tx3
Tx4
Rx5
Rx6
Rx7
Rx8
Inbound
Traffic
Set-up and Calibration:
F start – 50MHz
Stop – 20 GHz
Step – 25 MHz
Power – (-15 dBm)
Slope – (0 dBm)
Attenuation – (0dBm)
Averaging – ( Cat –1)
Measure – (Cat – 1)
IF BW – (100Hz)
Sweep Mode – Stepped
CAL: Thru Adapter / Phase Rotation
Config 1
Phase 1
Port Cal -> SOL CAL Kit Adapter
Phase 2 – Multiport (Press-Fit/Quick Connect Used)
Thru Cal -> Connect 1 -> 2
Connect 1 -> 4
Connect 3 -> 4
Connect 2 -> 3
Note: Terminate unused ports to Load
Phase 3 – SOL -> Connect:
Open to Port 1, 4, 3, 2
Short to Port 2, 1, 4, 3
Load to Port 3, 2, 1, 4
S-Parameter Procedure and Mapping

## Slide 11
Measurement:
F start – 50MHz
Stop – 20 GHz
Step – 25 MHz
Power – (-15 dBm)
Slope – (0 dBm)
Attenuation – (0dBm)
Averaging – ( Cat –1)
Measure – (Cat – 1)
IF BW – (100Hz)
Sweep Mode – Stepped
Labeling Convention:
Left Card – Prime
Right Card – Remote
Rx1
Rx2
Rx3
Rx4
Tx5
Tx6
Tx7
Tx8
Tx1
Tx2
Tx3
Tx4
Rx5
Rx6
Rx7
Rx8
Inbound
Traffic
S-Parameter Procedure and Mapping

## Slide 12
Measure Phase 1 (Create Folders 1-25m_Outbound_FEXT)
(Create Folder 1-25m_Outbound_NEXT)
Port: J2K2 Thru G2H2 ssj2k2g2h2 SN 004 (Backplane)
Phase 2 – Data Transforms – Select 2 balanced ports – OK
Save Data same label
Export s4p (mixed mode) transform same label
Crosstalk -> Drive j2k2 -> Listen quiet lines g3h3 (Rx1-4)
Save Data – FEXT folder
- example 1.25m (-35.376 dB)
Export Transform – Real/Imaginary
-> Drive j2k2 -> Listen g3h3 NEXT (Rx5-8)
Save Data -> Listen NEXT folder (-62.972 dB)
Export Ansoft s4p Transform – Real/Imaginary
-> Drive j2k2 -> Listen g2h2 Place in NEXT folder
Save Data -> Listen NEXT folder (-60.503 dB)
Export Ansoft s4p Transform – Real/Imaginary
Note: Terminate unused ports to Load
Rx1
Rx2
Rx3
Rx4
Tx5
Tx6
Tx7
Tx8
Tx1
Tx2
Tx3
Tx4
Rx5
Rx6
Rx7
Rx8
Inbound
Traffic
S-Parameter Procedure and Mapping

## Slide 13
1 m Prime Channel Differential Insertion Loss
1 m Prime Channel Differential Return Loss
Construction Notes:
Outbound
Channel routed in top of PCB.
Channel vias have significant
stub.
Top Plot:
Red – 1m Inbound Insertion Loss
- Y2
Blue – 1m Outbound Insertion Loss
- Y1
Construction Notes:
Inbound
Channel routed in bottom of
PCB.
Bottom Plot:
Red – 1m Inbound Return Loss – Y2
Blue – 1m Outbound Return Loss –
Y1
SDD11 and SDD12

## Slide 14
Top Plot:
Red – 1m Inbound FEXT – Y2
Blue – 1m Outbound FEXT – Y1
Bottom Plot:
Red – 1m Inbound NEXT – Y2
Blue – 1m Outbound NEXT – Y1
NEXT and FEXT

## Slide 15
Molex reference backplane
  1.0 m Nelco N4000-13SI with 2 GbX connectors
S-parameters measured
Single driven line crosstalk for each of four aggressors
  Single aggressors can be superimposed to simulate multiple driven line crosstalk
S-parameters demonstrate effect of an uncorrected 191.2 mil stub and bottom-side routed channel
Recommend the inclusion of this channel in the Backplane Ethernet simulation set
Conclusions