## Slide 1: Residential Ethernet Synchronization Schemes
Dirceu Cavendish, NEC

## Slide 2: Clock Synchronization Types
Network-synchronous approach: all devices are clocked from a common click or Primary Reference Clock (PRC).PRC and clock distribution scheme required.
TX and RX are clocked independently: slip buffers are used to smooth out any clock differences. Slow slip rate required. Network jitter has no effect on destination clock.
RX derives an estimate of the transmitter clock from the received data stream: PLL required to slave receiver clock to the master clock. Packet network jitter has a direct effect on clock estimation.

## Slide 3: Time Stamp Clock Synchronization
Characteristics
  No common network clock
  Timestamp send periodically between TX and RX.
    Period is smaller than smallest block size of data stream.
Network
Adaptor
TX
clock
oscillator
Pulse counter
Packet
Network
Jitter
Buffer
RX
clock
VCO or DCO
Pulse counter
+
-
PLL
Issues
  TX & RX clock frequency drift
  Packetization at TX
  Network jitter (queueing, muxing)
Loop
filter

## Slide 4: Time Stamp Clock Synch-PLL algo*
Set Loop filter parameters
Initialize variable
Error: e(0) = 0
Filter output: Nerr(0)=0
Arrival of first transmitter timestamp
Arrival index: n=0
Store timestamp value: T(0)
Store receiver counter value at arrival: R(0)
Arrival of next Kth (K>=1) transmitter timestamp
Arrival index: n=n+1
Store timestamp value: T(n)
Store receiver counter value at arrival: R(n)
Measure time interval between current and previous timestamp
(e.g. in clock cycles)
Transmitter interval measurement: T(n): T(n) – T(n-1)
Receiver interval measurementl: R(n) = R(n) – R(n-1)


Compute error in transmitter and receiver
Timestamp measurements
E(n) = T(n) - R(n)


Compute loop filter output
Ncorr(n)
DCO Input:
Ndco(n) = Nnom – Round[KoNcorr(n)]
VCO Input:
u(n) = Ncorr(n)
Source: “CES over Ethernet: Part 1: Clock synchronization using timestamps”,
J. Aweya, M. Ouellette, D. Y. Montuno, K. Felske, Int. Journal of Net. Mgm., 2004

## Slide 5: Payload playout with recovered clock
Data Buffer
(size of bound on delay variation)
Timestamp buffer
Data
Playout
Mechanism
+
-
PLL
Packet
Data
Timestamp
Jitter offset
Comparator
Receiver Frequency (bit timing)

## Slide 6: In Summary