## Slide 1: On LAA capabilities & scope
Dino Flore
Chairman of 3GPP RAN
(Qualcomm Technologies Inc.)
Notes: <number>

## Slide 2: Background
The IEEE LS in RP-150543 contains questions on
  LAA capabilities
  The solution developed by the LTE-U Forum, aka LTE-U
The above and the questions received during the presentations to IEEE and Wi-Fi Alliance reflect some industry confusions on the 3GPP LAA capabilities & scope
The goal of this document is to clarify these aspects

## Slide 3: LAA capabilities
RAN1 provided an interlocutory answer in RP-150551 to the IEEE questions related to the LAA capabilities, but doubts still remain outside 3GPP given that the detailed capabilities are discussed at end of the release
Also, from general 3GPP release perspective features are typically made optional or mandatory with an IoT bit, to allow phased deployment of the features in the market
Which has led some outside 3GPP to legitimately wonder what will happen when 3GPP defines the new 5 GHz band(s). Will it be possible to have 3GPP release-13 compliant products that operates in this band but do not support the LAA features?
The answer to the above question is NO

## Slide 4: LAA capabilities (cont’d)
Per current agreement 3GPP is committed to develop a single, global, solution addressing the regulatory constraints of the different regions
This means that 3GPP will mandate support of the essential LAA coexistence features in eNBs/UEs accessing the newly defined 5GHz unlicensed band(s)
  The essential LAA coexistence features will be the ones recommended by WGs to address the requirements of the various regions
  These will include the recommended scheme for LBT, discontinuous transmission with limited maximum transmission duration, etc..
Detailed coding of the above in the specs will be done when LAA is finalized and features are added in the specifications
  But 3GPP specs have multiple examples of features mandated for specific bands

## Slide 5: LAA scope & LTE-U
The proprietary coexistence mechanisms developed by the LTE-U Forum for the US market, aka LTE-U, have not been evaluated by 3GPP
As such LTE-U is not in scope of the current 3GPP LAA work and 3GPP cannot express any opinion on it