## Slide 1: Overview of the 802.10 SDE Protocol
Presented by Ken Alonge
Chair, 802.10

## Slide 2
Primary Goals of 802.10
Develop an interoperable security solution for all 802 MACs
  Security solution based on threat analysis (Annex 2A)
  Threat analysis determined security requirements
Security protocol independent of crypto mechanism & key management
Security services selectable (must have either confidentiality or integrity, can have both)
Support bridged environments
Enable coexistence of protected & non-protected frames

## Slide 3
Placement of SDE in the 802 Stack
LLC
MAC
SDE
Security
Applied
Security
Removed
USER
STACK 1
USER
STACK N
SYS
MGT
KEY
MGT

## Slide 4
Current SDE Header Format
DA
SA
CLEAR
HEADER
PROTECTED
HEADER
ICV
INTEGRITY PROTECTED
ENCRYPTED
DATA
PAD
STA
ID
FLAGS
FRAG
ID
SEC
LABEL
SDE
Des
SAID
MDF

## Slide 5
Clear Header Fields
M = Mandatory, if Clear Header is selected
O = Optional
SDE Designator (M) | Identify frame as having security protection
SAID (M) | Identify what security association to use to encrypt, integrity seal, or both
MDF (O) | Accommodation for a particular vendor’s proposed implementation

## Slide 6
Protected Header Fields
Station ID (O) | Origin authentication mechanism
Flags (O) | Identifies when fragmentation is enabled
Fragment ID (O) | Fragment counter
Security Label (O) | Enables application of access control security labels to frames
O = Optional

## Slide 7
SDE Header Format Modifications
DA
SA
CLEAR
HEADER
PROTECTED
HEADER
ICV
Current Format
Revised Format
INTEGRITY PROTECTED
ENCRYPTED
CLEAR
HEADER
PROTECTED
HEADER
DATA
ICV
INTEGRITY PROTECTED
ENCRYPTED
DA
SA
VLAN
TAG
PAD
DATA
PAD
STA
ID
FLAGS
FRAG
ID
SEC
LABEL
Pload
EType
FLAGS
FRAG
ID
SEC
LABEL
SDE
Des
SAID
MDF
SEQ
NO.
SAID
MDF
X
X
X
X
X = May be deleted

## Slide 8
SDE Designator
SDE designator is compatible with LLC
Going forward, use of an EtherType is more acceptable

## Slide 9
SDE in a Bridged Environment
Non-SDE
Bridge 1
Non-SDE
Bridge N
Unprotected Data
Environment
Trusted Enclave
Trusted Enclave
Unprotected Data
Environment
Protected Data Environment
Untrusted Network
SDE
Bridge A
SDE
Bridge B
X
Y

## Slide 10
Proposed PAR Purpose & Scope

## Slide 11: Purpose
The purpose of this PAR is to update the Secure Data Exchange (SDE) Protocol specified in IEEE Std 802.10-1998, to accommodate newly identified security requirements for all current 802 MACs and delete unneeded header fields.

## Slide 12: Scope
The scope of this PAR is to make changes to the format and processing of SDE PDUs to:
  Accommodate replay protection
  Integrity protect the Destination MAC address
  Integrity protect additional header fields, particularly the VLAN tag, as needed
The current PDU format and processing will have to be modified to incorporate a sequence number; the DA will have to be included in the computation of the ICV, and; the VLAN tag (and any other required header fields) will be included in the computation of the ICV, if protection is required by VLAN tagging rules (which are to be specified).
In addition, an informative annex will be developed that discusses various scenarios for securing Layer 2 bridged networks and a normative annex will be developed that defines an SDE profile specifying a single interoperable SDE configuration that must be supported by all vendors claiming conformance to the revised SDE specification.