## Slide 1: Secure Frame Format Proposal
SFF: PAR, Architecture, 5 Criteria,
Some ideas and notes
mick_seaman@ieee.org

## Slide 2: SFF Proposal : Agenda
Explain the key concepts behind the words of the PAR
Describe the architectural fit of this component of the security solution
Provide further material for the 5 criteria
Share some ideas about potential solutions and consequences

## Slide 3: Proposed Scope : Some words
To define a secure frame format to ensure the connectionless confidentiality of MAC Service Data Units (MSDUs) and to ensure data origin identification and the connectionless integrity of the MAC frames that convey these MSDUs using a secure association between MAC layer entities providing the MAC Internal Sublayer Service (-1-) or the MAC Enhanced Internal Sublayer Service (-2-). This proposed standard will not include key management but will make use of other projects to establish the secure association.
References: -1- IEEE Std 802.1D, -2- IEEE Std 802.1Q.

## Slide 4: SFF PAR Concepts
Communication between:
Peer media access method independent MAC layer entities:
Providing ISS (.1D) or EISS (.1Q)
With
Connectionless data integrity
Connectionless data confidentiality
Data origin authenticity

## Slide 5: Concepts : SFF Entities
Peers
Media access method independent
MAC layer entities
MAC Service Boundary
Media Access Method Dependent Functions

## Slide 6: Concepts : Internal Sublayer Service
ISS = MAC Service + MAC SA, FCS, access priority
EISS = ISS + VLAN ID
MAC Service Boundary
Media Access Method Dependent Functions

## Slide 7: Concepts : Connectionless data
Connectionless Service Provision
Each service request is independent of any other
  Delivery probability and ordering are aspects of QoS
Connectionless Service Support
Each service request is supported by a single frame transmission, not a sequence of related frames
Frames are mutually independent
  Agreed replay protection discussion is in PAR scope

## Slide 8: Concepts : Data integrity & confidentiality
Data integrity
Covers MAC DA, SA, VID*, user priority*, user data
Does not cover MAC dependent fields
Data confidentiality
Covers user data
  Possible interworking issues between .1D + SFF and .1Q + SFF
Does not cover MAC DA, SA, VID*, user priority*, MAC dependent fields

## Slide 9: Concepts : Data origin authenticity
Need to know which entity has ‘secured’ the data if not implicit at receiver, i.e. if ‘multihop’ or non-pt-to-pt
Integrity guaranteed
Confidentiality explicitly not provided
  Facilitate management observation
Confuse or optimize with key identity?
Field may be absent if pt-to-pt single hop
Field may be absent, if logical pt-to-pt single hop?
  System redundancy with LLID?

## Slide 10: Concepts : What’s not in
Denial of service
BUT after known time deltaT has elapsed after any attack has ceased the system is guaranteed to recover from the DoS

## Slide 11: SFF Architecture (likely consequences 1)
Secure association end points map to Ports (.1D, .1X)
Uncontrolled and Secured/Authorized Ports
  Address the bootstrap problem
  In principle could have multiple Ports, each corresponding to a number of security associations
MAC Service Boundary
Media Access Method Dependent Functions

## Slide 12: SFF Architecture (likely consequences 2)

## Slide 13: Notes : On a frame format
DA, SA
SFF TAG
  Key Identifier
  Data Origin (Securing Party) Identifier
VLAN TAG (optional)
User data
Integrity Check Value
Integrity
Confidentiality
optional
optional