## Slide 1: Deploying the world’s largest campus IEEE 802.11b network
IEEE 802.11 November 2003 Plenary
Tutorial #5 – Case Study
Tuesday, November 11, 2003
Albuquerque Convention Center – Ballroom A
Jonn Martell, Wireless Project and Service Manager
University of British Columbia
jonn.martell@ubc.ca

## Slide 2: About the presentation and presenter
Implementation of the world’s largest IEEE 802.11b network.
Showcase of IEEE standards in action.
Provide feedback to IEEE members on where implementers need help.
Jonn Martell
  15 years experience in network implementation.
  5+ years in wireless networking
  IEEE 802.11 member

## Slide 3: Agenda
Snapshot of wireless.ubc.ca
Education environments
Seamless campus-wide wireless network
End user experience
Wireless statistics and usage
Challenges
Key success factors
Network design
Security
Management
Futures and managed spectrum

## Slide 4: Snapshot of wireless.ubc.ca
Campus wide
Close to 5000 users
150 buildings
1300 Access Points (APs)
600 acres coverage
5 million square feet of coverage
Roaming enabled
Complete indoor and outdoor coverage
$5.9M CDN of a $30.6M connectivity project
Main campus completed (on time and on budget). Adding student residences.

## Slide 6: Education environments - EDUs
Usability is more important than security.
Mix of hotspot/public access and “enterprise” networking.
Four different types of users.
Relatively insecure indoor environments.
Very decentralised; leadership is only valued by addressing user needs.
High intellectual capability and autonomy.
Will always need wired connectivity for high bandwidth applications (like video and medical applications).

## Slide 7: Motivation for a seamless campus wide wireless network
There was a need, even two years ago!
Choice: Deploy as a campus wide network or deal with hundreds of poorly configured APs & incompatible domains.
Primary target, students and faculty are mobile and need campus wide access.
Need to be ready for future applications like mobile phones.
Need to avoid re-authentication issues between zones.
Segmentation done by user or traffic type, not geographically.

## Slide 8: End user experience
“Ease of use” and “zero cost” are the two prime goals.
Campus-wide coverage. Wireless only becomes truly useful when it’s available everywhere.
Needs to work with any IEEE 802.11 devices with no help desk support. Calls cost money (for everyone).
All Internet use is authenticated.
Faculty, Students and Staff self create campus wide accounts used for many services including wireless.
Faculty and Staff can “sponsor” guests and create accounts for them.
Legacy devices IEEE 802.11b are here to stay; we’ll always have insecure portions to support these devices.
But … also need to be able to support the latest standards (especially in regards to security).

## Slide 9: Wireless Network Use
email, calendaring, messenging.
Online voting, score keeping.
Instrumentation.
Wireless labs anywhere, anytime.
Futures
Utilities – cost savings in operations.
Voice over wireless (campus wide Wi-Fi cordless phones).
Wireless photocopier/printers.
We’ve seen nothing yet, we have to be able to support any applications.

## Slide 10
Usage - Monthly Unique Users

## Slide 11
Usage - Daily Unique Users

## Slide 12: Challenges
Delays with standards-based wireless security; had expected it in 2002.
Setting user and stakeholder expectations.
Network fragility (although 99.6% reliable in almost two years of operation).
Changing old models and legacy thinking.
Vendors who aren’t prepared for EDU environments.
“Technology surfing” & changing landscape.
Fuzzy standards with optional and incompatible technology: 802.11 FH versus DS, 802.3af options, 802.11e options.
RF is analog, networking is digital. RF is a whole new world where 50% signal is considered good and discards are tolerated.
Lack of true “virtual AP” capabilities.

## Slide 13: Key Success Factors
User-centric service.
Planning and research.
Shared vision of making UBC a top University.
UNP Project management framework.
Dedicated wireless project team.
A strong senior leadership and sponsorship.
A strong online communications strategy.

## Slide 14: Network Design
End-user experience drove the network design.
Isolation of insecure wireless network using logical and physical separation.
Segmenting by user & authentication type, not by geography.
Segmentation using campus-wide VLANs (IEEE 802.1Q).
Public address instead of NAT (RFC 1918) addresses; easier to track abuse.
Broadcast management using filtering and rate limiting.
Better broadcast is needed for Ethernet. IEEE 802.3ah will need to address large broadcast domains. Cable and DSL has already done this.
Except for small environments, difficult to see how to justify highly proprietary & specialized cores (standards as the base technology is critical).

## Slide 15: The Network

## Slide 16: Network Equipment
1300 Access Points – Cisco AP1200 (802.11b radio to be upgraded to 802.11g pending issue resolution).
200 distributions switches – Cisco 3550PWR (power over Ethernet) connected to Gigabit Ethernet (LX/SX).
4 core “carrier class” gigabit switches – Cisco 4507R (with redundant CPU and power).
Web authentication servers (redundant): Colubris CN3500.
VPN servers (to be redundant): Contivity 2700.
Redundant Firewalls and IDS servers: Cisco PIX (& various).
Redundant RADIUS servers: Radiator connected to six LDAP servers and then to Oracle.

## Slide 17: Security – still the #1 issue
Risk Management
Web-based authentication
VPN Authentication and Encryption
IEEE 802.1x authentication and encryption
Physical security
When solved, IEEE should co-host conference with Blackhat.com

## Slide 18: Web-based authentication
Simple, users bring up browsers: automatic redirection.
Users get started on their own: greater satisfaction and cheaper to operate. Similar to Hotspot models.
Secure (SSL/HTTPS) authentication.
Pass-through (unauthenticated) access to www.wireless.ubc.ca & www.library.ubc.ca
Status/session windows provides user feedback: login ID, time and bandwidth consumption. Helps prevent abuse.
Because HTTPS is not a stateful protocol, ARPs for duplicates and state.
Works with any wireless client although most PDAs don’t support popups for status window.

## Slide 19: VPN – Authentication and Encryption
Optional but highly recommended and included free as part of the service.
PPTPv2 support for simplicity
  Added MSChapV2 support on LDAP
  Many PDAs have PPTPv2 support
IPSec for security
Still too vulnerable to “man in the middle” at Layer 2 via ARP attacks (seen ettercap?) and other attacks.
Can provide virtual departmental VPN services using ID followed by dot department. user.department
VPN is not a very good technology for wireless, can’t handle fundamental wireless unreliability that well.
Managing risks
  How unsafe is PPTPv2?
  How safe is IPSec in various implementations?

## Slide 20: IEEE 802.1x – the strategic choice for wireless authentication and encryption
Not all EDUs are optimistic about IEEE 802.1x
802.1x is still not really deployable on a large scale without considerable pain (and costs).
To be a success, needs to be compatible with shipping laptops and PDAs.
WPA is a good start but Wi-Fi Alliance has no user advocacy group. They need to focus on delivering what users want not on vendor differenciation.
We need a neutral Interoperability certification body.
By doing login at AP, allows dynamic VLANs (equipment should not have a limited number of VLANs).
Too many EAP variations (and increasing all the time!)

## Slide 21: EAP
Pronounced “Eeeeeeeaapppp” Definition: What implementers say to themselves when they look at the implementation issues, uncertainties and variables.
Although implementers can control network and authentication backends, they can’t control clients.
We need strong standards and good deployment guides for this important part of the puzzle
The number of hours collectively wasted by implementers on EAP is a crime.
Too many types:
  EAP-TLS – it’s broken and should be easier to deploy
  EAP-Cisco (LEAP) – also broken and proprietary with no support from Microsoft.
  EAP-PEAP (is there a “standard” yet?)
  EAP-TTLS (no Microsoft support and the permutations are multiplied)
  EAP-SIM

## Slide 22: … EAP – what we really need
Best way to do wireless authentication: Distributing limited/throw-away certificates via secure Web downloads. These could be checked across domains. My certificates could be for martell.itservices.ubc.ca or martell.ca for example.
Would allow large wireless network operators to trust other domains. ubc.ca would setup trust relationships with other EDUs and with commercial Hotspot providers.
Certificates and certificate distribution needs to be inexpensive to be ubiquitous across different platforms.
By limiting the number of time a userID and password is used (tp infrequent management of certificates), limit exposure of ID/password theft.

## Slide 23: Filtering
Rogue DHCP
SNMP filtering
Microsoft Networking (NBT, RPC)
Can turn on PSPF on APs and Protected Port/PVLAN on switches
Might dramatically increase filtering when IEEE 802.1x (WPA/IEEE 802.11i) becomes deployable and/or if abuse increases.
Exercise in risk management.

## Slide 24: Physical Security
APs are the only device out of the wiring closet in typical enterprise installations
Forcing the AP in the closet isn’t ideal because of antenna cable loss and the fact that future cells might get smaller.
Good enclosures are hard to source, most commercial ones are metal (not RF friendly).
APs need to be able to authenticate to the switches (using IEEE 802.1x). If APs are unplugged the port is disconnected and left off. This needs to work on IEEE 802.1Q trunk ports.

## Slide 25: VLANs & Virtual AP support
IEEE 802.1Q (VLAN) is a great technology.
Currently can map multiple SSID to a single BSSID (not good enough and almost useless because of single BSSID limitations).
Currently have two SSIDs mapped to VLANs but expect to grow to many more.
True Virtual AP capabilities need the multiple BSSID support.
Provides semi “out of band” management by having a higher priority protected management VLAN for all wireless devices.
The need for dynamic VLANs. Ideal would be to have single VLAN per user and users could form groups by themselves.
In EDU environment, we will broadcast three base wireless networks “student”, “education” and “admin”. In corporate environment, there will be a need to have a “visitor” open (but authenticated) network. VLANs support on APs is a requirement for enterprise class APs.
Will likely keep existing “ubc” broadcast network as well as “ubcsecure” 802.1x protected network (WPA/802.11i)

## Slide 26: VLANs & Virtual AP support

## Slide 27: Authentication, Authorization and Accounting - RADIUS
At the heart of the wireless network.
Provides AAA services for Web login, VPN and 802.1x.
Goes against LDAP (high availability configuration).
Accounting info goes in enterprise SQL databases.
Track user ID, machine/Mac, IP, bytes, time (critical to get hogs and other abusers).

## Slide 28: Management
Devices are on a segmented VLAN not accessible from user or wireless networks.
Vendors tools aren’t there yet for large networks but we have an “off the shelf” network.
Lightweight tools versus expensive, complex and inflexible heavyweights.
All network devices also documented in databases.
Extensive SNMP based management via scripts and Intermapper
WLSE – Cisco’s AP management tool used to assist in RF data collection. Needs to have programmable interface. WDS needs to be ported to core switches.
Need physical security of AP or AP acting as 802.1x client to switches.

## Slide 31: Managing concurrent use

## Slide 32: Supporting Research
Massive test bed.
The need to balance operations with research.
Developed of Visual Mapping tool for recording survey information.
Automatic channel and power assignment technology under development (which we hope to “plug-in” to WLSE)
Other propagation studies underway:
  diversity antennas?
  overlapping channels?
  does a spectrum need to be managed to be reliable?

## Slide 33: Impact of newer standards
IEEE 802.11e? - QOS will be done on a per-VLAN basis. Telephony, transaction and management wireless vlans need highest priority. QOS threat is not from friendly or well behaved RF.
Fast Roaming – an absolute minimum to support and scale mobility. Need a good solution both at Layer 2 first and then at Layer 3 (and between other technology like 802.20)
802.11k - Radio resources: should also work to provide client assisted information and detect rogues & interference. Vendor implementations will likely lead the way in the short term.
Ideally, equipment should be able to run (with regulatory unlock code) on other spectrum around 2.4 GHz

## Slide 34: Future - Spectrum
Success of low cost, unlicensed spectrum is clear… but reliability and spectrum congestion is an issue.
Expanding the spectrum: the FCC & Industry Canada
  2001 Speech from the Throne: “…making broadband access widely available to citizens, businesses, public institutions and to all communities by 2005.”
2nd generation high speed wireless technology should provide reliable and cost effective networking using:
  commodity products
  low power regulations (smaller “markets”)
  inexpensive “managed” spectrum
  municipal and campus licenses
IEEE 802.20 – future high speed mobile broadband?

## Slide 35: Spectrum auctions are not the solution
Current Industry Canada logic
  “Auctions offer a number of advantages over the other options that are available to governments to assign access to the radio spectrum such as: their ability to promote economically efficient use of spectrum; their openness and objectivity as an assignment mechanism; their procedural efficiency; and their ability to return appropriate compensation to Canadian taxpayers for the use of a public resource.”
  “The Government’s objective in conducting auctions is not to raise revenue, but rather to award licences fairly, efficiently and effectively so as to ensure that the Canadian public derives the maximum possible benefit from the spectrum resource.”
  “Auction bids thus depend on consumer prices; consumer prices do not depend on auction bids.” Reference
This logic doesn’t work when if consumer price goal is “zero cost”.

## Slide 36: Questions
Information on UBC Network www.wireless.ubc.ca
Email contact:
  Work: jonn.martell@ubc.ca
  Personal: jonn@martell.ca