## Slide 1: Authentication and Key Agreement
  Flexibility in credentials
  Modern, publically analysed/available cryptographic primitives
  Freshness guarantees
  PFS?
  Mutual authentication
  Identity hiding for supplicant/end-user
  No key re-use
  Fast re-key
  Fast handoff
  Efficiency not an overarching concern:
    Protocol runs only 1/2^N-1 packets, on average
  DOS resistance

## Slide 2: Credentials flexibility
Local security policy dictates types of credentials used by end-users
Legacy authentication compatibility extremely important in market
Examples:
  username/password
  Tokens (SecurID, etc)
  X.509 certificates

## Slide 3: Algorithms
Algorithms must provide confidentiality and integrity of the authentication and key agreement.
Public-key encryption/signature
  RSA
  ECC
  DSA
PFS support
  D-H

## Slide 4: Freshness
Most cryptographic primitives require strong random material that is “fresh”.
  Not a protocol issue, per se, but a design requirement nonetheless

## Slide 5: Mutual Authentication
Both sides of authentication/key agreement must be certain of identity of other party.
Symmetric RSA/DSA schemes (public-keys on both sides)
Asymmetric schemes
  Legacy on end-user side
  RSA/DSA on authenticator side

## Slide 6: Identity hiding
Important to hide end-user identity in some situations (public shared networks, for example).
  DISTINCT from hiding MAC address
IPSEC has gone down this road, and has much experience.
Not as easy as it sounds—active attacks make it harder.

## Slide 7: Fast rekey/fast handoff
Ability to create fresh keying material without undergoing slow authentication path (requiring username/password again, for example).
In mobile environments, ability to transition without re-doing initial authentication.

## Slide 8: Efficiency
CPU efficiency not a serious concern, since this protocol will be used relatively infrequently.
On-the-wire efficiency may be important in low-bandwidth scenarios, but again protocol is not run that often, compared to MACsec.

## Slide 9: DOS resistance
Modern key-agreement protocols fertile ground for DOS attacks.
Look to other schemes (IKE, for example) to provide guidance.
No perfect anti-DOS schemes
  Increase unpleasantnesss for attacker
  Detect and throw away bogosity at the earliest, cheapest point in the protocol.